## Slide 1: Considerations on NTN for Rel-18
RWS-210394
3GPP TSG RAN Rel-18 Workshop 28 June-2 July 2021 Online
Source: Ericsson Agenda Item: 4.2 Document for: Discussion

## Slide 2: NR NTN Status Quo (Rel-17) (Architecture)
Transparent architecture
  gNB on the ground
  Transparent (bent pipe) satellite: Uu terminated on the ground
  All network interfaces terminate on the ground
    No specific statement for Xn functions for NTN (i.e. current specification seems enough)
      Cell reconfiguration for energy saving
      Resource coordination
      Load management
    SON specifically for NTN not supported
    Xn interface management not precluded
    Xn between HAPS and local terrestrial neighbors not precluded

## Slide 3: NR NTN Status Quo (Rel-17) (Mobility)
Mobility (including e.g. TN-NTN) pending RAN2 progress
  Large propagation delays, especially for GEO: RTT =~550 ms
  Frequent HOs for LEO: satellite visibility time from a UE is in the order of minutes
  Propagation delay will interrupt data transmission by several RTTs before connections are established to target cell
    Potentially large interruptions with existing HO mechanism
  Potential solution (proposed in RAN2, discussion yet to start): consider Reduction of User Data Interruption (RUDI) HO with enhanced make-before-break for NTN
    To allow a UE with single RX/TX to extend the connection to source cell, minimizing HO interruption time (R2-1914724)

## Slide 4: NR NTN in Rel-18
Future scenarios may require even more flexibility and higher data rates for NTN
No particular need for “network-side” TN-NTN coordination (including mobility) was identified in Rel-17 that cannot be met with current Xn signaling
On the other hand, Xn functionality within the NTN itself is likely to become beneficial: the satellite as the gNB
  Inter-satellite mobility, DC, resource coordination, load management
  It is likely existing Xn functions can be reused
Regenerative architecture with full gNB on board was already studied in Rel-16
  ”No showstoppers”, no protocol adaptations seem needed (TR 38.821 Conclusions)
On mobility, the same constraints will still be present as in Rel-17

## Slide 5: Proposals
If NTN work is approved as part of Rel-18:
  Regenerative architecture with full gNB on board should be the regenerative architecture of choice
  RUDI HO with enhanced make-before-break should be added as mobility enhancement if not already part of Rel-17

## Slide 6
https://www.ericsson.com/en/5g