## Slide 1: On flexible spectrum usage in Rel-18
RWS-210402
3GPP TSG RAN Rel-18 workshop
Electronic Meeting, June 28 - July 2, 2021‎
Document for: Discussion
Agenda Item: 4.1
China Academy of Telecommunications Technology (CATT)

## Slide 2: Motivation
Fragmented spectrum resources in different frequency bands, in particular in low frequency bands, e.g. 700MHz/800MHz/900MHz
  Large overhead of common signals incl. e.g. SSB, SIB etc., in each carrier in each frequency band
  Larger bandwidth is desired to achieve higher UE throughput
  Long (de-)activation of SCell(s) delay in CA framework
  Complicated mobility management/measurement
  Sync/QCL assumptions can be inferred across multiple frequency bands

## Slide 3: Solution
Serving Cell over Multi-Band (SCoMB)
  A serving cell includes multiple carriers within a frequency band or across multiple frequency bands
Potential benefits
  Reduced overhead of common signals
  Fast carrier switching/activation
  Simplified/better management of mobility
  Less scheduling overhead

## Slide 4: Scope of work
Configuration of a serving cell with multiple carriers
Scheduling/resource allocation/transmission/feedback within a serving cell with multiple carriers
  Fast carrier switching among the carriers within a serving cell
  A single DCI scheduling PDSCH/PUSCH across multiple carriers
  Resource allocation of PDSCH/PUSCH across multiple carriers
  A single or multiple TB transmission across multiple carriers and the HARQ-ACK feedback mechanism of the TB(s)
Co-existence with legacy UE if any
Mobility/measurement enhancements with a serving cell with multiple carriers

## Slide 5: Summary
This contribution discuss flexible spectrum usage in Rel-18. More specifically, Serving Cell over Multi-Band (SCoMB), where a serving cell includes multiple carriers within a frequency band or across multiple frequency bands, is elaborated.
Proposal 1 RAN takes into account the benefits of SCoMB as shown in slide 3, and considers it as one of the Rel-18 topics for further discussion.