## Slide 1: On UL MIMO enhancements in Rel-18
RWS-210403
3GPP TSG RAN Rel-18 workshop
Electronic Meeting, June 28 - July 2, 2021‎
Document for: Discussion
Agenda Item: 4.1
China Academy of Telecommunications Technology (CATT)

## Slide 2: UL MIMO – Current Status
UL MIMO has been lagging behind DL in feature richness
  Core features inherited from LTE
Moderate enhancement in Rel.15 - 17
  more focused on FR2.
  Less enhancement in FR1

## Slide 3: Motivation for UL MIMO innovation
New business scenarios
  Mid/short range applications, medium to (very) low mobility
  Home entertainment, office/stadium, business
  Data-heavy UL: video surveillance/uploading, wireless drone, coal mine monitoring, police/military/public safety, vehicle-to-vehicle
  Ultra-high-density uplink:
New device:
  Less power/computation constraints than traditional MBB devices
  XR terminal
  IAB node
  Indoor/outdoor access point, relay node
  Medical, robot, drone
  V2X road site units
  Commercial/industrial surveillance devices

## Slide 4: Motivation for UL MIMO innovation (cont.)
New carrier frequency
  Further higher carrier frequency up to 71GHz
  Even more challenging propagation calls for advanced multi-antenna innovation
New system bandwidth
  BW up to 400MHz (compared to 20MHz@ LTE)
New operation paradigm
  AI/ML: where a good system model is lacking, or too complicated to be tractable

## Slide 5: UL MIMO - Potential Enhancement Areas
UL frequency selective precoding
  Wideband precoding leading to low precoding granularity and multiuser scheduling gain
  Up to 30% cell-average and 60% cell-edge throughput gain is achievable by frequency-selective precoding
Beam management enhancements with multi-panel TX and multi-panel/TRP RX deployment
  Pre-Rel-18 NR device can only choose one panel for UL transmission, unable to fully utilize UL device investment (e.g. multiple PA and panels)
  Joint transmission enabling multiple panels simultaneously is promising, considering multi-panel, multi-site and multi-RSU scenario
Higher-order UL-MIMO
  Extension to 8 layer UL MIMO can bridge the gap with DL performance, especially for advanced wireless nodes
  Enhancement areas include SRS, UL codebook, control channel extension
Ultra-high-density UL-MIMO
  DMRS overhead reduction