## Slide 1: On XR in Rel-18
RWS-210411
3GPP TSG RAN Rel-18 workshop
Electronic Meeting, June 28 - July 2, 2021‎
Document for: Discussion
Agenda Item: 4.2
China Academy of Telecommunications Technology (CATT)

## Slide 2
A Rel-17 SI is ongoing on XR (RP-210460‎), which covers multiple use cases such as VR, AR and cloud gaming (from TR26.928). These use cases generally have stringent requirements on data rate and E2E latency.
The main focus of the study is to figure out the traffic model XR/CG‎, and to establish a set of evaluation methodology along with KPIs, so that the further performance evaluations are possible.
Although the studies are ongoing, one could observe that the main KPIs concern a few important aspects, i.e.,
  DL and UL capacity,
  UE power consumption, and
  Overall performance which takes power/capacity/latency into account.
Background

## Slide 3
As summarized in RP-210459, the 60Mbps, 30Mbps are among the required bitrates used for evaluating XR/CG performance. Depending on the traffic model, the actual requirement to throughput can be even larger, e.g., due to burst nature of the data.
Although detailed evaluations are still to be done in the Rel-17 SI, one could expect the capacity issue in dense populated scenarios, or for the case when only limited system bandwidth is available.
This limits the user experience as only a fraction of the UEs could be served.
Capacity
Chart: Percentage of UE that 99% of packet successfully transmitted within 10ms with 100MHz BW
| 4 | 6 | 8 | 10 | 12
30Mbps | 1 | 1 | 1 | 0.975 | 0.896
45Mbps | 1 | 0.986 | 0.968 | 0.792 | 0.646

## Slide 4
As shown in TR 26.928, certain XR services require E2E latency on the order of tens of ms or up to a few hundreds of ms. Such latency budget shall also address the processing time at device side as well as in the CN.
In some cases, packet delay budget around 10ms needs to be fulfilled.
Such tight requirement limits the flexibility of link adaption, as well as scheduling in either frequency or spatial domain.
Latency
Chart: Percentage of UE that 99% of packet successfully transmitted within PDB
| 4 | 6 | 8 | 10 | 12
PDB=5ms | 0.9583 | 0.8056 | 0.5938 | 0.375 | 0.1319
PDB=7ms | 1 | 0.9583 | 0.8438 | 0.6833 | 0.3889
PDB=10ms | 1 | 0.986 | 0.968 | 0.792 | 0.646

## Slide 5
As stated in the SID RP-210410, the power issue can be more outstanding for the XR/CG terminal than smart phone.
TR 26.928 gives many cases that requires frame per second on the order of 60-90. This essentially means the packet interval a few tens of ms, which makes many power saving mechanism (e.g., DRX) less efficient.
Power consumption
Power Saving Scheme | Mean PS gain | #satisfied UEs per cell / #UEs per cell
W/o C-DRX | - | 9.75 / 10
C-DRX 1 (8,4,2) | 15.45 % | 6.17 / 10

## Slide 6
Rel-17 study is ongoing on evaluation methodology for XR/CG performance.
Great challenges are foreseeable in terms of capability, latency, and power consumption, in order for a good user experience.
Given the multiple factors that impact the E2E user experience, it is meaningful to study on a good metric for QoS measurement in RAN.
Proposal 1 Quality of service for XR/CG service should be measureable in RAN to understand the real gap.
Proposal 2 Based on Rel-17 studies, further enhancements can be introduced to tackle the issues on capability, latency, and power consumption
Summary