## Slide 1: Satellite/NTN network solutions - operators’ perspectives
RWS-210421
Agenda Item: 4.3
Type: Discussion
Document for: Discussion
RAN-Rel-18 workshop June 28 – July 2, 2021
Source: Hughes/EchoStar, Inmarsat

## Slide 2: Release 18 - NTN Enhancement key objectives
  Increase scalability to support different satellite deployment scenarios, satellite payload and UE architectures cost-effectively
  Improve waveform energy efficiency to match and exceed existing SatCom waveforms

## Slide 3
Consider Hybrid Solutions: GEO – MEO – LEO
  Service Continuity – High availably offered by all constellation
  Latency - Minimize latency by sending time-critical messages through LEO and high-volume, latency insensitive traffic through GEO
  Capacity - Maximize throughput during peak traffic with both available paths
  System Performance -Improve availability through diversity and added redundancy
MEO use cases - presently the NR-NTN standardization work is focused on LEO (600 km & 1200 km) and GEO scenarios. We suggest that MEO scenarios should be studied within the Rel-18 framework. Recognizing that some aspects of the LEO and GEO solutions would apply for MEO scenarios as well, other considerations specific to MEO should be investigated.
  NOTE: MEO is already included in the NTN-IoT TR 37.763.
Both Earth-fixed and earth-moving beams for NGSO, Earth-fixed for GEO.
Enhance support for VSAT UEs in high frequency satellite bands to enable as relays.
Deployment Scenarios

## Slide 4: NTN enhancements in Rel-18
Improve waveform energy efficiency to match and exceed existing SatCom waveforms including support for NOMA schemes
Dual connectivity to support service continuity between NTN and TN
Increase bandwidth granularity to support smaller bandwidth configurations (current 5 MHz minimum BW is too large for some system architectures)
Consider low-PAPR waveform options (such as DFT-s-OFDM in DL) and identify PAPR reduction techniques

## Slide 5: IoT NTN specific enhancements in Rel-18
Enhancements to spectrum efficiency for very low SNR use cases including indoor/NLoS coverage
Further study of HARQ benefits to IoT NTN
UE power efficiency enhancements
Support for smaller bandwidth configurations and connected mobility
Consider IoT NTN DL channel capacity enhancements and support for NOMA schemes in UL