## Slide 1: MBS Enhancement for 5G-Advanced
3GPP TSG RAN Rel-18 workshop
Electronic Meeting, June 28- July 2, 2021
Source: ZTE, Sanechips
Agenda: 4.2
RWS-210473

## Slide 2
Background
What Rel-17 MBS WID (RP-201038) aimed to:
  introduce support of Multicast and Broadcast services into 5G NR for the first time
  define the basic functions of MBS reception/delivery for UE in different RRC states
  focus on NR as the RAT, with forward compatibility of other RAN architecture
  minimize UE complexity which means Rel-15/16 UE capability as design reference
The reality is:
  pure e-meeting with compromised productivity/meeting progress
    RAN1 neglects many key optimizations due to lack of TUs
    RAN2 important features like mobility have not been touched for three consecutive meetings
    RAN3 session management has been affected by not-so-stable SA2 normative work
  a bunch of key features de-prioritized
Further enhancements for MBS in RAN1/2/3 are needed in Rel-18

## Slide 3
Overview of Enhancements for Rel-18 MBS (part 1)
Layer 1 Centric Enhancements
  Reliability/Efficiency Enhancement for RRC_IDLE/INACTIVE UEs
  Throughput Enhancement for RRC_IDLE/INACTIVE UEs
  CFR Enhancement for RRC_IDLE/INACTIVE UEs
  Enhancement to Enable Unicast and MBSFN based MBS Simultaneously
  Enhancement to Partial Beam Sweeping of MBS transmission
Potential Architectural Enhancements

## Slide 4
1-1 Reliability/Efficiency Enhancement for RRC_IDLE/INACTIVE UEs
gNB may not be able to obtain UE's channel state for MBS in RRC_IDLE/INACTIVE states
  massive UEs entering connected state just for channel state report is NOT efficient or even NOT possible
  some UEs belonging to other operators are even NOT able to enter connected state for feedback
    UEs from different operators may be served by one MBS service provider
  gNB may have to employ the most conservative Tx parameters for MBS transmission in RRC_IDLE state just like MIB/SIB, which extremely lowers system efficiency
Potential enhancements for Rel-18 MBS
  support of UE's feedback (e.g., CSI/HARQ-ACK/best SSB) in RRC_IDLE/INACTIVE states can be considered for MBS in Rel-18 to enhance reliability and efficiency of MBS transmission
Refer to R1-2100109 for details

## Slide 5
1-2 Throughput Enhancement for RRC_IDLE/INACTIVE UEs
Broadcast traffic will boost with the growth of MBS market and emerging new applications
  currently, carrier aggregation (CA) are only allowed for RRC_CONNECTED UEs.
  massive UEs entering connected state to be configured with CA to increase the MBS throughput occupies too much network resources. Many UEs may be rejected to enter RRC_CONNECTED UEs.
  support CA for RRC_IDLE/INACTIVE UEs can boost the broadcast throughput.
Potential enhancements for Rel-18 MBS
  support carrier aggregation for RRC_IDLE/INACTIVE UEs
    PSS/SSS, MIB, SIB and paging are transmitted in PCell
    one or multiple SCells can configured by SIB together with PCell for MBS transmission
    one cell (either PCell or SCell ) can be selected by UE for PRACH/msg3 transmission

## Slide 6
1-3 CFR Enhancement for RRC_IDLE/INACTIVE UEs
Effectively and flexibly extending MBS resources in RRC_IDLE/INACTIVE states is desired as MBS traffic will boost with the growth of the market
Some constraints to CFRs (depending on Rel-17 conclusions) in RRC_IDLE/INACTIVE states will limit MBS resource extension or limit the access to MBS service for low-capacity UE (e.g., Redcap UE), e.g.
  only supporting one CFR
  location constraint among CFRs as well as between CFR and initial BWP
Potential enhancements for Rel-18 MBS
  remove or relax the location constraints among CFRs as well as location constraints between CFR and initial BWP in RRC_IDLE/INACTIVE states
  support more than one CFR
e.g., when it is required that one CFR is covered by another CFR as shown in the right figure, the UEs being interested in MBS1 must have larger bandwidth capability

## Slide 7
1-4 Enhancement to Enable Unicast and MBSFN based MBS Simultaneously
MBSFN transmission can boost MBS performance greatly
In Rel-17, MBSFN can be supported by implementation and no optimization is done
MBSFN transmission may need different numerology from unicast transmission, e.g., longer CP
Some UEs may have unicast and MBS traffic simultaneously where MBS PDSCH is transmitted in MBSFN manner
Potential enhancements for Rel-18 MBS
  Enhancement to enable simultaneous configuration of unicast PDSCH and MBSFN-based MBS PDSCH in Rel-18, e.g., support of two BWPs with different numerologies, one for unicast and another one for (MBSFN-based) MBS

## Slide 8
1-5 Enhancement to Partial Beam Sweeping of MBS transmission
In Rel-17, full beam sweeping (similar to Rel-15 SIB) transmission associated with SSBs has been supported for RRC_IDLE/INACTIVE states
Any optimization on beam sweeping scheme is treated with low priority for MBS transmission in RRC_CONNECTED state, which are targeted to a group of UEs distributed in only part of beams
  Full beam sweeping may be unsuitable from the perspectives of DL overhead and gNB power
  It is also not applicable to perform beam change for a UE by updating the TCI state of a CORESET, as the CORESET may be shared by multiple UEs
Further, MBS transmission to UEs in RRC_ CONNENTED state with all SSB beams will also lead low efficiency.

## Slide 9
1-5 Enhancement to Partial Beam Sweeping of MBS transmission - Cont'd
MBS transmission with Partial Beam Sweeping in desired beam directions can be further considered in Rel-18
  For RRC_CONNECTED state, either SSBs or CSI-RSs can be used for partial beam sweeping transmission
  For UEs in RRC_IDLE/INACTIVE states with best SSB feedback, SSBs can be used for partial beam sweeping transmission
Potential enhancements for Rel-18 MBS
  Beam management for partial beam sweeping: Configuring the association between MOs and part of RSs, dynamic selection of MO/CORESET for monitoring PDCCH of MBS transmission
  HARQ-ACK feedback scheme (e.g., DAI/Feedback resource determination) for partial beam sweeping

## Slide 10
Overview of Enhancements for Rel-18 MBS (part 2)
Layer 1 Centric Enhancements
Architectural Enhancements
  Supported RAN Architecture for Multicast Services
  UE RRC States & RAN Context Management for Multicast Services
  Service Continuity/Mobility for Multicast Services
  Other (e.g., enhancements to Broadcast services)

## Slide 11
2-1 Supported RAN Architecture for Multicast
RAN Architecture for Multicast
  a majority view that the WI in Rel-17 shall focus on stand-alone architecture
  support of dual connectivity/multiple cell reception not clear (deprioritized in Rel-17) but can be low hanging fruit
  might limit MBS deployment flexibility if not supported
Potential enhancements for Rel-18 MBS (RAN3, RAN2)
  support flexible MBS deployment in NRDC, and in Multiple cells
SN: where MBS is already available or more suitable for MBS deployment
MN: UE' s MCG where UE control planes lies

## Slide 12
2-2 UE RRC states & RAN context management for Multicast services
UE RRC states & RAN context management for Multicast
  focused on RRC_CONNECTED states only (other case deprioritized in Rel-17)
  might not meet services requirements on scalability/service continuity in cases of massive UE being served by the same MBS service, the network might be congested due to maintaining of large number of UEs in RRC_CONNECTED states (e.g., TR 23.774)
Potential enhancements for Rel-18 MBS (RAN2, RAN3)
  Multicast reception support in RRC_INACTIVE states
  Mechanisms for PTM configuration reception/update/release for UE in RRC_INACTIVE
  UE RRC states transitioning, mobility and service continuity in RRC_INACTIVE

## Slide 13
2-3 Service continuity/mobility enhancement for Multicast services
Service continuity/mobility for Multicast services
  Aligned with Rel-15 mobility design (other variations being deprioritized in Rel-17) to have service continuity for Multicast through unicast like mechanism
  Lossless support still being debated in RAN2/3 whether such feature shall be supported considering the architectural impacts, and “basic mobility support” is only pursued as indicated in Rel-17 WID
Potential enhancements for Rel-18 MBS (RAN2, RAN3)
  Advanced HO support for Multicast services, e.g., CHO, DAPS, to further enhance the mobility robustness, reduce the service interruption during mobility
  Lossless support of Multicast HO for certain Multicast services

## Slide 14
2-4 Other architectural enhancements
Other architectural enhancements worth a bit attention if not covered in Rel-17:
  Broadcast delivery which inherit the framework from LTE eMBMS including the design flaws (e.g., one MCCH for all), further power efficiency enhancement for delivery mode 2 reception
  Area specific PTM configuration
  MBSFN support. Architectural perspective, e.g., deployment scenarios, RAN architectural impacts including whether new network entity is needed, or limited in single gNB/gNB-CU, and inter-network entity coordination
Potential enhancements for Rel-18 MBS (RAN2, RAN3)
  further power efficiency enhancement for delivery mode 2 reception
  Area specific PTM configuration
  MBSFN support including architectural enhancement, group scheduling for MBSFN, related Uu signaling design

## Slide 15
Conclusion - Potential Rel-18 NR MBS Enhancement
Layer 1 centric enhancements:
  Support feedback for RRC_IDLE/INACTIVE UEs (RAN1, RAN2)
  Support carrier aggregation for RRC_IDLE/INACTIVE UEs (RAN1, RAN2)
  Flexible CFR configuration for RRC_IDLE/INACTIVE UEs (RAN1, RAN2)
  Enable reception of unicast and MBSFN based MBS Simultaneously (RAN1, RAN2)
  Support Partial Beam Sweeping in desired beam directions (RAN1, RAN2)
Architectural enhancements:
  Flexible MBS deployment in NRDC, or in Multiple cells (RAN3, RAN2)
  Multicast recetpion support in RRC_INACTIVE states (RAN2, RAN3)
  Advanced and lossless HO support for Multicast services (RAN3, RAN2)
  Other enhancements on Broadcast services, e.g., power efficiency enhancement, area specific PTM configuration, MBSFN (RAN3, RAN2)

## Slide 16: Thanks