## Slide 1: Support of UAV for 5G Advanced
3GPP TSG RAN Rel-18 workshop
Electronic Meeting, June 28- July 2, 2021
Source: ZTE, Sanechips
Agenda: 4.2
RWS-210474

## Slide 2: Motivation on the NR-UAV
Cellular enabled UAV(drone) is beneficial for various application, e.g.,:
  Vertical application including agriculture, power line inspection, surveillance and logistics
  Platoon communication
  Drone-based gNB/Relay for on-demand communication
  Personal entertainment for flight experience
which is already specified for LTE and more tighter requirement including SA’s needs should be considered to enable the vertical usage in NR:
Application | Coverage type | Throughputs requirements |  | Latency |  | Positioning | Region
 |  | DL | UL | Control | Data |  | 
Logistics | seamless coverage with altitude below 100 m | 300Kpbs | 25Mbps | <20ms | <200ms | <0.5m | Urban/Suburban/Rural
Agriculture | fixed region with altitude below 200 m | 300Kbps | 30~120 Mbps | <20ms | <200ms | <0.1m | Rural
Monitoring /Surveillance | fixed region or predefined route with altitude below 100 m | 600Kbps | 30~120 Mbps | <20ms | <200ms | <0.5 m | Rural/Urban

## Slide 3: Identified issues for NR-UAV
For achieving the target, followings should be considered:
  UAV identification and control, e.g.,
    Lawful interception
    Flight path control
    Access restriction for network
  DL enhancement to ensure continuous service, e.g.,
    Enhancement on mobility including measurement and reporting
    Optimization on transmission for UE including beam management

## Slide 4
For achieving the target, followings should be considered:
  UL performance improvement, mainly target for interference mitigation, e.g.,
    Co-channel interference cross UE within same and different cell.
    Cross-link interference cross UE within different cells
  Additional use case to take Drone as BS
  RF/RRM definition for new UE type or BS type (if Drone as BS is supported)

## Slide 5: Objectives for NR-UAV for 5G Advanced
Study the cross-link interference condition [RAN1]
Specify enhancements on performance:
    Power control for random access (RAN1)
    The height-dependent BM mechanism for both FR1/FR2(RAN1)
Specify side-link enhancements for UAV, e.g., . broadcast of identifiers (RAN1/2)
Specify enhancements on access control, e.g., regulation indication (RAN2/3)
Specify enhancements on mobility (RAN2):
    Report mechanisms, e.g., new event to reduce the report overhead.
    Conditional HO, e.g., based on location information, UE’s airborne status, flight path plan, etc.
  Specify subscription and identification(RAN2/3)
  Specify RF and RRM core requirements for gNB and UE (if new UE type/BS type is identified)

## Slide 6: Thanks