## Slide 1
3GPP TSG RAN Rel-18 Workshop RWS-210506
e-Meeting, June 28 – July 2, 2021
Visible Light Communication for 5G Agenda Item: 4.1
Notes: Pas de S à science, digital science.

## Slide 2: Motivation
Free-space Optical (FSO) communications should be considered as a 5G technology which is complementary to radio but sharing NR air-interface
  Currently License-free and wideband
  Two potential scenarios
    Coupled with lighting (VLC) for low-cost high-bandwidth MIMO-OFDM indoor communications
    Efficient and radio-interference free medium-range NG/F1 links outdoors
  Higher-degree of security because of localized communications
  Potential for high-accuracy indoor localization (VLC).
Key challenges
  Seamless integration with 3GPP radio architecture in the above scenarios
  Propagation modeling

## Slide 3: Scenario 1 : VLC over NR Target Deployment Scenario
Well-lit Indoor (airport, shopping-center factory, office)
LED lamp based
Hybrid VLC/Radio for 3GPP-access
  Supplemental-DL optical component carriers with UL on conventional radio infrastructure
  Use existing R15/16/17 MIMO-OFDM on optical carriers
Centralized gNB-DU with distributed analog VLC RU TX, MIMO via multiple-LED interfaces in each lamp
gNB-DU
(TX)

## Slide 4: Scenario 2 : NG/F1 links
Use infra-red laser for sub-1km links to gNB (NG) or gNB-DU (F1)
  Radio-based gNB at street-level
  >10 Gbps FSO links
Main target
  Metropolitan deployment of street-level gNB
    Fixed access on roof or side of buildings

## Slide 5: Ideas for Studies
Scenario 1
  Detailed architecture proposals for
    DL-only VLC-based carriers
    for distributed resource allocation (beamforming) and point-to-point MIMO
  Indoor propagation models and VLC performance requirements
Scenario 2
  Multi-beam Infrared backhaul/midhaul based on NR (Point-to-multipoint topologies)
  Protocol extensions for tunneling F1/NG inside NR RAN
  Outdoor metropolitan Infrared propagation models