## Slide 1: Evolution for Coverage Enhancement in Rel-18 Agenda Item: 4.3
3GPP TSG RAN Rel-18 Workshop RWS-210507
e-Meeting, June 28 – July 2, 2021
Notes: Pas de S à science, digital science.

## Slide 2: Motivation
Coverage of UL Channels (PUCCH, PUSCH) is the bottleneck in many important scenarios [TR 38.830]
Rel-17 solutions are based on repetition
During the SI phase, novel improved PUCCH formats were proposed and showed significant performance gains compared to Rel-15
Due to higher specification impact those solution were deprioritized in the WI phase
Rel-18 must strive to specify improved PUCCH formats

## Slide 3: Design Principles
Small Payloads: < 9 bits
DMRS-less orthogonal signal sets
Low decoding complexity
Large Payloads: 11/22 bits
Low PAPR sequence + structured code
Optional: Unequal error protection
Low PAPR sequence + signal code

## Slide 4: Example of Potential Coverage Gain
0.5 dB coding gain + 4.8 dB PAPR gain = 5.3 dB compared to PUCCH Format 3
Coding gain can be increased by relaxing the PAPR requirements
11-bit Transmission
TDL-D LOS 30ns delay-spread
14 symbols, 1 PRB
no frequency hopping

## Slide 5: Conclusion
Still significant potential for coverage gain via improved PUCCH transmission schemes
Include specification of enhanced PUCCH formats in Rel-18