## Slide 1
3GPP TSG RAN Rel-18 Workshop RWS-210508
e-Meeting, June 28 – July 2, 2021
Considerations for Sporadic
Random Access in Massive IoT
Use Cases Agenda Item: 4.2
Notes: Pas de S à science, digital science.

## Slide 2: Motivation
Massive machine-type communications would benefit from a low-latency uplink for short packets
  Minimize UL transmissions and time/energy to upload sporadic short packets
  Event-driven traffic (sensor networks)
    Physical phenomena detection (earthquake, gas leak, electricity grid anomalies, etc.)
    Autonomous vehicle warning systems
    gaming
    => all have potentially massive UL measurements contending for the channel
Question: What is the shortest time to send a single user-plane (IP) packet with the 5G air-interface (R16) from RRC_INACTIVE
  2-step RACH MsgA/B (RRCResume), DCCH/ULSCH with BSR (RRCResumeComplete),DCI0_x,DTCH/ULSCH => still lots of exchanges for a single packet
  AND scheduler knows this is a critical sporadic UL transmission to minimize scheduling time => difficult with large user-populations and event-driven traffic!

## Slide 3: Proposal
Study techniques to minimize channel access for single UL U-plane packet from RRC_INACTIVE
  Ideally a single UL transmission with high probability => high-reliability of first transmission
Consider joint Layer1/Layer2 approaches to guarantee minimal access time for
  Large user-populations (insufficient PRACH resources for orthogonal multiple-access => NOMA)
  Time/frequency channel uncertainty with relaxed frequency offset requirements