## Slide 1
3GPP TSG RAN Rel-18 Workshop RWS-210651
e-Meeting, June 28 – July 2, 2021
Considerations for Sporadic
Random Access in Massive IoT
Use Cases Agenda Item: 4.2
Notes: Pas de S à science, digital science.

## Slide 2
Motivation
Massive machine-type communications would benefit from a low-latency uplink for short packets
  Minimize UL transmissions and time/energy to upload sporadic short packets
  Event-driven traffic (sensor networks)
    Physical phenomena detection (earthquake, gas leak, electricity grid anomalies, etc.)
    Autonomous vehicle warning systems
    gaming
=> all have potentially massive UL measurements contending for the channel
Question: What is the shortest time to send a single user-plane (IP) packet with the 5G air-interface (R16) from RRC_INACTIVE
  2-step RACH MsgA/B (RRCResume), DCCH/ULSCH with BSR (RRCResumeComplete),DCI0_x,DTCH/ULSCH => still lots of exchanges for a single packet
  AND scheduler knows this is a critical sporadic UL transmission to minimize scheduling time => difficult with large user-populations and event-driven traffic!
14/06/2021
- p 2

## Slide 3
Background
Rel-17 RAN2 WI Small Data Transmission (SDT) addresses this problem
  RA-based approach allows UL data transmission in MsgA/Msg3
  RO and/or preamble partitioning indicates SDT event
  Payloads of 100 – 300 Bytes are considered
  Up to two preambles groups to indicate PUSCH-config (payload size)
  In 2-step RACH the PUSCH transmission is contention-based
Observations:
  Contention in massive access use-cases
    PRACH/PUSCH resources on initial BWP are limited
  UL resources are used inefficiently
    Limited number of PUSCH configurations not adapted to channel conditions
  Consider smaller payloads for cyber-physical use cases (~tens of Bytes)
14/06/2021
- p 3

## Slide 4
Proposals
Study techniques to minimize contention
  Consider joint Layer1/Layer2 approaches to guarantee minimal access time
  Improved UE signaling techniques to indicate UL transmission requirements (TBS/MCS)
In massive-access scenarios investigate
  How to handle many contending UEs with unknown channels?
  In case of DMRS-based transmission, how to estimate channels for many overlapping UEs?
14/06/2021
- p 4