## Slide 1: FL plan on L1 enhancements for LTM at RAN1#113
3GPP TSG RAN WG1 #113 R1-2304588
Incheon, Korea, May 22nd – May 26th, 2023
Document For: Information
Agenda item 9.10.1
Source: Moderator (Fujitsu, MediaTek)

## Slide 2: Discussion plan

## Slide 3: Summary of RAN1#112(Feb) and 112b-e(Mar)
RAN1#112 (Feb)
  In RAN1#112, most of discussion time was pent on L1 measurement configuration, and hence sufficient time cannot be given to other important topics such as reporting, beam indication etc.
    In short, the overall progress was not so good
  However, FL believes the technical discussions were good enough to reach a lot of important agreements in April meeting.
RAN1#112bis-e (April)
  While we had important agreements for some topics (Baseline format of L1 measurement report, Beam indication by Rel-17 Unified TCI based TCI state index, and introduction of TCI state activation)
  No consensus on “no consensus”  FL is afraid that companies still focus on optimization/non-hopefull topics

## Slide 4: Goal of RAN1#112b-e(April) and 113(May)
RAN1#112b-e (April)
  Considering the remaining time for Rel-18 competition (1 e-meeting and 2 F2F meetings), FL sees the strong necessity to focus on the essential issues.
    The list of essential issues are provided in the next slide
  Non-essential/optimization issues will be treated on best-effort basis
RAN1#113 (May)
  Follow-up discussions on the essential issues will be performed
  Based on the agreements in RAN1#112b-e, discussion on RRC parameters needs to be commenced.

## Slide 5: Detailed plan for each meeting
Meeting No | Key issues | 
RAN1#113 (May) | Essential issues [Update of RAN1 assumptions on L1 intra- and inter frequency measurement – no strong need for RAN1 discussion in #112b-e] Configurations for L1 measurement – necessary configuration parameters, including time domain information Contents of gNB scheduled L1 measurement reporting (concluding how to choose the beams for reporting followed by how many, how/whether to configure/activate the beams of the cells etc.) Preparation for cell switch and beam indication: Details on DL synchronization Beam indication for scenario 2 based on Rel-17 unified TCI framework (beam indication applies to signals/channels that does not follow Rel-17 unified TCI, and beam indication for multiple target cells [followed by beam application time]) [Simultaneous operation of Rel-17 ICBM and Rel-18 LTM – maybe UE capability discussion: TBD] Information included in cell switch command RRC parameters | Low priority issues CSI-RS based L1 measurement L1-SINR Filtering for L1 measurement results Additional container for gNB scheduled L1 measurement reporting (i.e. MAC CE) UE/event triggered reporting Preparation for cell switch and beam indication: TRS tracking and CSI acquisition Beam indication for scenario 1 Beam indication applicable to gNBs supporting only Rel-15 TCI framework
RAN#100 (June) | TBD | 
red part: handled by Fujitsu
blue part: handled by MediaTek

## Slide 6: RAN1 agreements and FL plans for RAN1#112b-e
L1 measurement

## Slide 7: L1 measurement: L1 Intra-freq measurement
[Conclusion at RAN1#110b-e]
Agreement
For Rel-18 L1/L2 mobility, L1 intra-frequency measurement for candidate cell is supported
  At least the following aspects are for RAN1 further study:
    RAN1 assumes Rel-17 ICBM CSI measurement as starting point.
    Whether and how to apply relaxation for the restrictions imposed on the Rel-17 intra-frequency L1 non-serving cell measurement defined in 9.13.2 of TS38.133, where RAN4 impact is foreseen, e.g.
      SFN offset alignment compared with serving cell
      BWP setting, i.e. non-serving cell SSB should be covered by serving cell active BWP
      Introduction of symbol level gap or SMTC for larger Rx timing difference (i.e. larger than CP length)
    Commonality with intra-frequency L3 measurement
    Commonality with L1 inter-frequency measurement for measurement configuration
Send an LS to RAN4 (CC RAN2)
  RAN1 to ask RAN4 if the restriction on e.g., SFN offset alignment, BWP setting and Rx timing difference, etc, described in 9.13.2 of TS38.133 for intra-frequency L1 non-serving measurement can be relaxed or not.
  RAN1 assumes Rel-17 ICBM CSI measurement as starting point.
  [Conclusion at RAN1#111, #112, #112bis-e]
  No discussion, wait for RAN4 LS

## Slide 8: L1 measurement: L1 Inter-freq measurement
[Conclusion at RAN1#110b-e]
Agreement
For Rel-18 L1/L2 mobility, further study the potential RAN1 spec impact of L1 inter-frequency measurement
  The definition and scenarios of L1 inter-frequency measurement is determined by RAN4, and RAN1 assumes at least the following until receiving their confirmation
    The scenarios not included in intra-frequency are regarded as inter-frequency, which includes at least the following scenarios:
      The frequency of the measured RS not covered by any of the active BWPs of SpCell and Scells configured for a UE, but covered by some of the configured BWPs of SpCell and Scells configured for a UE.
      The frequency of the measured RS not covered by any of the configured BWPs of SpCell and Scells configured for a UE
  At least the following aspect is studied:
    Commonality with L1 intra-frequency measurement for measurement configuration
Send an LS to RAN4 (CC RAN2)
  RAN1 would like to confirm our understanding that the supported scenarios not included in intra-frequency are regarded as inter-frequency, which includes at least the following scenarios:
    The frequency of the measured RS not covered by any of the active BWPs of SpCell and Scells configured for a UE, but covered by some of the configured BWPs of SpCell and Scells configured for a UE.
    The frequency of the measured RS not covered by any of the configured BWPs of SpCell and Scells configured for a UE
  It is RAN1 understanding that the introduction of measurement gap and SMTC for L1 inter-frequency measurement, if any, is expected to be a RAN4 issue
  Note: this content is included in the LS agreed for intra-frequency L1 measurement
[Conclusion at RAN1#111]
Agreement
For Rel-18 LTM, L1 inter-frequency measurement is supported from RAN1 point of view.
[Conclusion at RAN1#112, 112bis-e]
No discussion, wait for RAN4 LS

## Slide 9: L1 measurement: L1 intra- and inter-freq measurement
SSB-based Intra-frequency L1 measurement:
  Center frequency and SCS of the SSB of the candidate cell are the same as those for serving cells, which is indicated in ServingCellConfigCommon
  For the time offset,
    The SFN offset alignment can be relaxed if UE performs L3 measurement before L1 measurement (FL note: it is not clear if this has any RAN1 spec impact – and maybe none)
    The scenario that RTD between the SSBs of serving cell and candidate cell on the same carrier is larger than CP length of the corresponding SCS is supported with additional UE capability.
      The UE capability is discussed and defined in RAN4
  For the BWP setting,
    The SSB for intra-frequency L1 measurement may not be covered by serving cell active BWP at least in some scenario.
      The definition of the scenario is determined by RAN4
SSB-based Inter-frequency L1 measurement:
  The supported scenarios not included in intra-frequency L1 measurement are regarded as inter-frequency L1 measurement.
Because RAN4 agreements for the definition of intra-frequency L1 measurement include many FFS, FL sees no strong necessity to update the RAN1 agreements at RAN1#113.
Definition of L1 measurement based on the RAN4 LSs:

## Slide 10: L1 measurement: Measurement RS
Given the controversy so far, this topic will just consume the online time in RAN1#113
  Spec impact and RAN4 workload
  Necessity and benefit on top of SSB based L1 measurement
Rel-18 LTM functionality can be completed without CSI-RS based L1 measurement: SSB-based measurement is anyway available
[Conclusion at RAN1#110b-e]
Agreement
For Rel-18 L1/L2 mobility,
  SSB is supported for L1 intra-frequency measurement
  SSB is supported for L1 inter-frequency measurement if inter-frequency L1 measurements are supported
Further study the following L1 measurement RS for candidate cell
  CSI-RS for tracking, beam management, CSI and mobility, CSI-IM, which is for L1 intra-frequency and L1 inter-frequency (if supported)
[Conclusion at RAN1#111]
The FL proposal 1-4-v3 was not due to the lack of time during RAN1#111. Companies are encouraged to perform their analysis based on the latest proposal below:
For Rel-18 LTM,
  L1 measurement based on CSI-RS for beam management for candidate cells is supported for L1 intra-frequency measurement and L1 inter-frequency measurement if supported in RAN4
    The definition of intra- and inter- frequency for CSI-RS is defined in RAN4
    The CSI-RS is explicitly linked to a candidate cell
    Applicability to L1-RSRP and/or L1-SINR is separately discussed.
    FFS for the support of other CSI-RS types (i.e. tracking, CSI, mobility and CSI-IM).
[Conclusion at RAN1#112]
No consensus on the following proposal (No time to come back), postpone to the next meeting.
[Working assumption: CSI-RS is introduced for L1-RSRP measurement from RAN1 point of view
  Intra- and inter- frequency is supported
  At least CSI-RS for BM [mobility] is supported
  Send an LS to RAN4 to explicitly ask their feasibility to finalize their work in Rel-18]
[Conclusion at RAN1#112bis-e]
- No discussion due to the lack of time
This topic will be discussed on low priority basis

## Slide 11: L1 measurement: Measurement quantity
It is pointed out that the benefit of L1-SINR cannot be achieved by SSB, but CSI-RS
However, the introduction of CSI-RS has not been agreed yet
Also, companies have a different understanding on the benefit of L1-SINR
[Conclusion at RAN1#110b-e]
Agreement
For candidate cell measurement for Rel-18 L1/L2 mobility,
  L1-RSRP is supported for intra-frequency candidate cell measurement.
  Further study the following measurement quantities for candidate cell measurement
    L1-RSRP for inter-frequency (if supported)
    L1-SINR for intra-frequency and inter-frequency (if supported)
FFS: to assess the use case and the benefit of UL measurement instead of/in addition to DL L1 measurement, which includes:
  How the UL measurement result is used, e.g. handover decision
  Signals/channels used for UL measurement, e.g. SRS
  Spec impact including other WGs, e.g. definition of gNB measurement, interface to transfer RS configuration or measurement results
  Note: The next discussion will take place based on companies’ contribution in future meeting.
[Conclusion at RAN1#111]
Agreement
For candidate cell measurement for Rel-18 LTM,
  SSB based L1-RSRP is supported for intra-frequency measurement
  SSB based L1-RSRP is supported for inter-frequency measurement from RAN1 point of view
  FFS: L1-SINR, CSI-RS based L1-RSRP
[Conclusion at RAN1#112]
No consensus on the following proposal
[CSI-RS based L1-SINR (with channel measurement and interference measurement using CSI-RS) is introduced from RAN1 point of view
  If supported, both intra- and inter-frequency L1-SINR is supported
  Send an LS to RAN4 to explicitly ask their availability in Rel-18]
[Conclusion at RAN1#112]
No discussion due to the lack of time and consensus on CSI-IR
L1-SINR discussion will be deprioritized in RAN1#113

## Slide 12: L1 measurement: Filtering for L1 measurement results
[Conclusion at RAN1#110b-e]
Postponed (FL proposal 1-6)
For Rel-18 L1/L2 mobility, [study the importance of mitigating the ping-pong issue for L1/L2 mobility, which is expected to align with RAN2. If important yes,] further study at least the following mitigation aspects:
  UE-based filtering to the L1 measurement results, where the definition of filtering includes:
    Time domain filtering: e.g. exact definition of time domain filtering, and/or
    Cell-level (spatial domain) filtering: e.g. how many beams are averaged, and/or how the beams are chosen.
  Applicability to L1-RSRP and L1-SINR (if supported)
  Applicability to intra-frequency and inter-frequency (if supported)
  Necessity to be specified in standard considering the presence of alternative implementation-based solutions, e.g. gNB-based filtering and/or L3 measurement (when involved)
[Conclusion at RAN1#111]
Given the comments from companies, FL believes no positive result can be obtained on this topic even when we discuss the discussion in this meeting. Therefore, FL would like to take approach 1 this meeting and to encourages to have offline discussions for the next meeting.
With this analysis, the discussion on this section is closed. If companies have any comments, the following table can be used or further input.
[Conclusion at RAN1#112, 112bis-e]
No discussion
FL plan is to deprioritize this discussion in RAN1#113,
and FL summary will not be prepared for this topic

## Slide 13: L1 measurement: Configurations for L1 measurement - 1
[Conclusion at RAN1#112]
Agreement
For L1-RSRP measurement RS configuration
  For SSB based L1-RSRP measurement:
    As a starting point, at least the following information needs to be provided to a UE, e.g.
      For intra- and inter- frequency: PCI or logical ID (e.g., as being defined in R17 ICBM), time domain (e.g. SMTC or periodicity and SSB position in burst)
      For inter-frequency: frequency domain location (e.g. center frequency), SCS
      FFS: transmission power (for pathloss calculation)
    Note: other parameters included in the configuration can be further discussed
    Including above agreement into the LS
  The detailed design of RRC structure is up to RAN2, and send an LS to RAN2 to request to work on the RRC structure design on the measurement configuration.
    Following RAN1 understanding will be provided in the LS
      RAN1 has discussed the following configuration options for L1 measurement configurations for SSB till RAN1#112:
        Option 1) Configurations for L1 measurement RS is provided under ServingCellConfig for the serving cells
          is useful to reuses the mechanism for Rel-17 ICBM and necessary information to support inter-frequency measurement will be added there.
        Option 2) Configurations for L1 measurement RS is provided separately from ServingCellConfig for the serving cells and CellGroupConfig for the candidate cells
          is useful to avoid the duplicated configurations for L1 measurement RSs, [and avoid UE to process configurations for L1 measurement RS provided under CellGroupConfig for the candidate cells]
        Option 3) Configurations for L1 measurement RS is provided under CellGroupConfig for the candidate cells
          can achieve the similar benefit as Option 2) by directly referring to the candidate cell configurations.
      Note RAN2 has a full flexibility to design the whole RRC structure design.
      RAN1 believes this is RAN2 expert region, and respectfully asks RAN2 to finalize the RRC structure design after RAN1 finalizes the discussion on RRC parameters.
      It is noted that RAN1 foresees the necessity of similar discussions on TCI state pool for candidate cells and L1 measurement report configurations.
[Conclusion at RAN1#112bis-e]
Agreement
RRC parameter ss-PBCH-BlockPower for candidate cells is included in the LTM configuration.
  UE needs the parameter to (at least) perform RACH towards candidate cells
  Note: how to capture this parameter and RRC structure are up to RAN2
Decision on {SMTC}/{periodicity and SSB position in burst} is needed for RRC parameter discussion.
One potential approach is to discuss this issue directly in RRC parameter session.
At the final round of email discussion in RAN1#112bis-e, many companies showed their views that choice of SMTC or periodicity and SSB position in burst can be left to RAN2
  This approach may be risky because RAN1 hasn’t sent any clear message to RAN2 to ask so

## Slide 14: L1 measurement: Configurations for L1 measurement - 2
Agreement
Send an LS to RAN2/RAN3 asking the clarification on intra-/inter-DU scenario:
  RAN1 has started the discussion on the configuration for L1 measurement and TCI states for candidate cells. Regarding the following RAN2 agreements captured in RAN2 LS (R1-2208331/R2-2209257), it is not clear for RAN1 which kind of information/configuration for candidate cell(s) are available at a serving cell for inter-DU case for Rel-18 L1/L2 mobility. Thus, companies have different understanding on the implication of the sentence “as much commonality as reasonable” in the LS.
    The design for intra-DU and inter-DU L1/L2-based mobility should share as much commonality as reasonable. FFS which aspects need to be different.
  RAN1 respectfully asks RAN2 and RAN3 if the serving DU knows the measurement RS configuration and TCI state configuration of cells served by another DU
Reply from RAN2 (R2-2212988) available
  RAN2 assumes that LTM (intra DU and inter DU) is network-controlled mobility where the control is from the source, i.e., measurements (L1 measurements) are configured in the UE from the source Cell, and the decision to switch cell is by the source cell, and enhancements considered for LTM before cell switch, e.g. pre-synchronization, TA handling, target beam management (to the extent it is supported) may be made by the source cell. RAN2 understands that this may require cooperation among source DU, CU, target DU, and/or OAM. RAN2 don’t see any blocking issue to share information between DUs but the support of this is in RAN3 domain. RAN2 see no necessity for a direct inter-DU-interface to support this.
Reply from RAN3 (R3-226829) available
  Regarding Q3 about L1 measurement and TCI state configurations in the LS, RAN3 agreed that based on the current specification, the serving DU cannot know the measurement RS configuration and TCI state configuration of cells served by another DU.
  Any possible consideration for Rel-18 on the coordination over F1 among serving DU, target DU, and CU would need clearly identified requirements from other groups.
RAN1 needs to define a clear requirement to RAN3 to move forward.
The necessity of further LS on this matter depends on the agreement in RAN1#113.

## Slide 15: RAN1 agreements and FL plans for RAN1#112b-e
L1 measurement reporting

## Slide 16: L1 measurement reporting – Contents of gNB scheduled L1 measurement reporting
Resolution on FFSs are necessary in RAN1#113
  FFS: How to select the L cells and M beams per cells is up to UE  Essential
  other UE capabilities are FFS  The maximum value of M x L needs to be decided. Other values can be left to UE capability discussion
  FFS if UE is allowed to report less than M x L beams  Optimization ? needs justification
  FFS: The following configurability is introduced in the report configuration  still some companies are not convinced with the necessity/essentiality.
Some other open issues exist
  Quantization (7bit absolute value and 4bit differential value: Can this mechanism reused? )  Essential
  Necessity of activation procedure, i.e. reporting is performed within the set of activated RSs in configures RSs
[Conclusion at RAN1#110b-e]
Agreement (FL proposal 2-1-1)
For L1 measurement report for Rel-18 L1/L2 mobility, further study the following mechanisms:
  Report as UCI on PUCCH or PUSCH
    Periodic report on PUCCH, semi-persistent report on PUCCH/PUSCH, and aperiodic report on PUSCH
    Further study potential enhancements to Rel-17 ICBM report format to accommodate Rel-18 scenarios, e.g.
      Inter-frequency measurement, if supported
      Increasing the maximum number of reported beams, which is 4 for Rel-17 ICBM
      Flexible size beam report, e.g. two-part UCI (e.g., the 1st part contains the best beam/cell and the number (e.g., N) of reported beams/cells, the 2nd part contains the rest (N-1) beams/cells
      Reducing the reporting overhead by e.g. choosing beams/cells per frequency or across frequencies to report (FFS how)
  Report on MAC CE
    Both gNB scheduled and/or UE initiated (if supported) report are studied
[Conclusion at RAN1#112bis-e]
Agreement
For the beam selection for SSB based L1-RSRP measurement report,
Beam selection is performed across the L cells from configured (or activated, if introduced) cells, i.e. M beams for each of the L cells
  FFS: How to select the L cells and M beams per cells is up to UE
M x L beams are reported in a single report instance
  Max values of M and L are based on UE capability, and at least M x L=4 is supported as a UE capability, other UE capabilities are FFS
    FFS if UE is allowed to report less than M x L beams
  The values of M and L are configured to the UE in the reporting configuration
FFS: The following configurability is introduced in the report configuration
  1) Whether serving cell is always selected in the L cell selection performed by the UE, and applicable when a UE is configured with L>=2
  2) at least one of the inter-frequency cells is always selected in the L cell selection performed by the UE, and applicable when a UE is configured with L>=2 and at least one cell in inter-frequency
Focus on Essential parts in RAN1#113, other parts can be discussed best effort basis
High Priority

## Slide 17: L1 measurement reporting - Container of gNB scheduled L1 measurement reporting
[Conclusion at RAN1#110b-e]
Agreement (FL proposal 2-1-1)
For L1 measurement report for Rel-18 L1/L2 mobility, further study the following mechanisms:
  Report as UCI on PUCCH or PUSCH
    Periodic report on PUCCH, semi-persistent report on PUCCH/PUSCH, and aperiodic report on PUSCH
    Further study potential enhancements to Rel-17 ICBM report format to accommodate Rel-18 scenarios, e.g.
      Inter-frequency measurement, if supported
      Increasing the maximum number of reported beams, which is 4 for Rel-17 ICBM
      Flexible size beam report, e.g. two-part UCI (e.g., the 1st part contains the best beam/cell and the number (e.g., N) of reported beams/cells, the 2nd part contains the rest (N-1) beams/cells
      Reducing the reporting overhead by e.g. choosing beams/cells per frequency or across frequencies to report (FFS how)
  Report on MAC CE
    Both gNB scheduled and/or UE initiated (if supported) report are studied
[Conclusion at RAN1#111]
Agreement
For gNB scheduled L1 measurement report for Rel-18 LTM, report as UCI is supported
  Semi-persistent report on PUSCH, and aperiodic report on PUSCH are supported
    FFS: periodic and semi-persistent PUCCH
  In a single report instance, report for serving cell and candidate cell(s) for intra-frequency and/or inter-frequency can be included.
[Conclusion at RAN1#112bis-e]
Agreement
Periodic and semi-persistent report on PUCCH are also supported for gNB scheduled L1-measurement reporting
FL thinks the important discussions on the container have been completed.

## Slide 18: L1 measurement reporting - Configuration for gNB scheduled L1 measurement report
FL has no plan to discuss the existing parameters for legacy L1 measurement reporting under this AI
  This is what companies expected in RAN1#112bis-e
  All the necessary discussion can be done under RRC parameter session
Other necessary discussions on new parameters can be discussed based on companies’ contributions
[Conclusion at RAN1#110b-e]
No consensus on the following FL proposal
For L1 measurement report configuration for gNB scheduled reporting, companies are encouraged to study the following proposals until RAN1#113
  At least the following RRC parameters needs to be provided to a UE, e.g
    Resource for channel measurement (i.e. SSB and CSI-RS if agreed) with the indication of associated cell, and exact indication signaling is up to RAN2, e.g. the indication can be explicit or implicit.
      a set of initial activated RSs/cells, if activation of RSs/cells are introduced
    Type of report configuration, i.e. periodic/semi-persistent/aperiodic
    Uplink resource configuration in order to report serving cell and candidate cell L1 measurement result to serving cell
    Quantity, if agreed
  The detailed design of RRC structure is up to RAN2, and the similar options for L1 measurement RS are further considered in RAN2

## Slide 19: L1 measurement reporting – UE/event triggered reporting
[Conclusion at RAN1#111]
Agreement
For L1 measurement report for Rel-18 L1/L2 mobility, if UE event triggered report for L1 measurement is supported based on further study
  At least the following aspects may be considered
    How to define UE event and exact definition of events,
    Report container
    Resource allocation/assignment for UE event triggered report
    Necessity of indication to gNB when the condition UE event is met, and how
    Necessity to define the condition to start/stop the reporting,
    Contents of the report/reporting format, PCI, RS ID, measurement result etc.
    The interaction with filtered L1 measurement results (if supported)
    Support of simultaneous configuration of both UE event triggered and any of periodic/semi-persistence/aperiodic reporting, and solutions when both of them are configured.
    Report destination, whether the report is sent to serving cell only or can be sent to one or more candidate cell(s).
    Benefit when L3 measurement is involved
[Conclusion at RAN1#112bis-e]
FL proposed Alt 2, but no consensus achieved
Alt 1 (Open issues are highlighted with yellow shadow)
UE event triggered report for L1 measurement is supported with the following design principle:
  Supported the following trigger events (FFS on the necessity of modification) where the threshold and offset value (if needed) is configured by RRC
    A3 based/Neighbor becomes amount of offset better than Pcell/PSCell;
    A5 based/Pcell/PSCell becomes worse than absolute threshold1 and neighbor/Scell becomes better than another absolute threshold2;
  As for Start/Stop condition:
    Time To Trigger (TTT) is introduced and time duration (FFS exact values) is configured by RRC, where UE event triggered report is performed when the configured event is continuously fulfilled within the configured time duration.
    The report is performed only once after the fulfillment of the event, i.e. no stop condition is defined
  No indication to notify the fulfillment of the event condition to gNB is introduced
  MAC CE is used to convey the UE event triggered report
    The scheduling of PUSCH is up to gNB
  Contents/format defined for gNB scheduled reporting is reused as much as possible (FFS the modifications)
  FFS: No filtering mechanism in time domain and cell level is introduced for L1 measurement results, i.e. use L1 measurement result or L3 measurement result (i.e. time domain filtering and/or cell level filtering)
  No specific enhancement on report destination is necessary, i.e. UE follow the gNB indication of Tx spatial filter and pathloss reference RS using the existing mechanism
  gNB scheduled reporting and UE event triggered reporting can be simultaneously configured
Alt 2. (if Alt 1 is not agreed in this meeting)
  No consensus to introduce UE event triggered report for L1 measurement results in Rel-18
FL plan is to deprioritize this discussion in RAN#113
FL thinks this is an optimization given the support of gNB scheduled reporting
Also, it will take long time to complete this functionality as proponents have different proposals

## Slide 20: RAN1 agreements and FL plans for RAN1#112b-e
Beam indication

## Slide 21: Beam indication - Beam indication mechanism based on Rel-17 unified TCI framework - 1
[Conclusion at RAN1#110b-e]
Agreement(FL proposal 3-1)
RAN1 to further study if the beam indication of candidate cell(s) L1/L2 mobility should be designed for a specific TCI framework below, and their potential RAN1 spec impact.
  Option A: Beam indication for Rel-18 L1/L2 mobility is designed based on Rel-17 TCI framework mechanism
  Option B: Beam indication for Rel-18 L1/L2 mobility is designed based on Rel-15 TCI framework mechanism
  Option C: Beam indication for Rel-18 L1/L2 mobility is designed based on both Rel-15 and Rel-17 TCI framework mechanisms
[Conclusion at RAN1#111]
Agreement
The beam indication of candidate cell(s) for Rel-18 LTM should be designed based on the following:
  Beam indication for Rel-18 LTM is designed based on Rel-17 unified TCI framework, if both serving cell and candidate cell support Rel-17 unified TCI framework
  FFS: whether/how to design mechanism for Beam indication for Rel-18 LTM when at least one from serving cell and candidate cell supports only Rel-15 TCI framework.
  Note: How and whether to indicate the new serving cell(s) and timing for beam indication are separately discussed
[Conclusion at RAN1#112]
Agreement
At least for Rel-17 unified TCI framework based beam indication included in cell switch command (i.e. scenario 2), beam indication applies to signals/channels that follow or are configured to follow Rel-17 unified TCI at the target cell(s)
FFS: beam indication for mTRP case
The following proposals are postponed
The existing mechanism, i.e. simultaneousTCI-UpdateList1 and simultaneousTCI-UpdateList2, is reused to indicate TCI states for multiple target cells
Beam application time may be different from that for Rel-17 ICBM, FFS the exact value(s)
[Conclusion at RAN1#112bis-e]
Agreement
Adopt Alt.2 for beam indication of target cell(s) and TCI state activation for candidate cell(s) (if supported) ,
  Alt. 1: By indicating RS identifier, i.e. mapping between RS identifier and Rel-17 unified TCI state is done by a UE
  Alt. 2: By indicating Rel-17 TCI state index
The following proposal was Postponed
For beam indication of target cell based on Rel-17 unified TCI framework applied to CORESET#0 and CORESETs (other than CORESET#0) associated with Type 0A/1/2-PDCCH CSS sets where no TCI state activation is provided, followUnifiedTCI-state is not enabled or not provided, the following alternatives are further studied, and one alternative will be down-selected at RAN1#113.
  Alt.1: Follow the indicated TCI state until a new TCI state is configured or activated by the target cell
  Alt.4: No new behaviour is introduced on top of Rel-17 unified TCI
High Priority
RAN1 needs to continue the discussion on the beam indication applies to signals/channels that “does not” follow Rel-17 unified TCI at the target cell(s)
  Alt1, Alt 4 or other approach ??  FL wants to conclude this issue in RAN1#113 (if no agreement is reached, it means that gNB scheduler shall avoid the problematic case)

## Slide 22: Beam indication: Configuration for TCI states based on Rel-17 unified TCI framework
FL sees the necessity of more discussion on the interpretation of unifiedTCI-StateType-r17
  unifiedTCI-StateType-r17 is a part of serving cell configuration and candidate cell configuration.
  unifiedTCI-StateType-r17 for target cell(s) is needed at a UE when TCI state activation is performed
  Then the question is which unifiedTCI-StateType-r17 applies to candidate cell TCI state?
    unifiedTCI-StateType-r17 for serving cell
    unifiedTCI-StateType-r17 for each candidate cell
    new unifiedTCI-StateType-r17 configured in serving cell configuration for each candidate cells
This may have a dependency how the TCI state pool is constructed
  Separate TCI states for LTM (from Rel-18) or Joint TCI state pool for LTM (with Rel-17)
[Conclusion at RAN1#112bis-e]
FL proposed conclusion
Similar as r17 TCI state mode indication with unifiedTCI-StateType-r17, Per candidate cell TCI state mode is provided before cell switch command to UE to determine the type of TCI state indication in the cell switch command
The discussion on this topic in RAN1#113 will be based on the companies’ contributions.

## Slide 23: Beam indication - Beam indication mechanism applicable to gNBs not supporting Rel-17 TCI framework
Given the remaining time of Rel-18 and the level of companies’ interest, FL sees no necessity to spend our time on this topic in RAN1#113
  It is important to finalize Rel-17 unified TCI framework based mechanism first
[Conclusion at RAN1#110b-e]
Agreement(FL proposal 3-1)
RAN1 to further study if the beam indication of candidate cell(s) L1/L2 mobility should be designed for a specific TCI framework below, and their potential RAN1 spec impact.
  Option A: Beam indication for Rel-18 L1/L2 mobility is designed based on Rel-17 TCI framework mechanism
  Option B: Beam indication for Rel-18 L1/L2 mobility is designed based on Rel-15 TCI framework mechanism
  Option C: Beam indication for Rel-18 L1/L2 mobility is designed based on both Rel-15 and Rel-17 TCI framework mechanisms
[Conclusion at RAN1#111]
Agreement
The beam indication of candidate cell(s) for Rel-18 LTM should be designed based on the following:
  Beam indication for Rel-18 LTM is designed based on Rel-17 unified TCI framework, if both serving cell and candidate cell support Rel-17 unified TCI framework
  FFS: whether/how to design mechanism for Beam indication for Rel-18 LTM when at least one from serving cell and candidate cell supports only Rel-15 TCI framework.
  Note: How and whether to indicate the new serving cell(s) and timing for beam indication are separately discussed
[Conclusion at RAN1#112]
FL proposal
Interested companies are encouraged to check the proposal on by proponent companies, and to input their contribution to the future meeting as necessity.
[Conclusion at RAN1#112bis-e]
No FL proposal was made
No time was spent in RAN#112bis-e for this issue because no time was available. With this, the discussion in this section is closed
This topic will be deprioritized at RAN1#113.

## Slide 24: Beam indication: Timing of beam indication – scenario 2 except TCI state activation
[Conclusion at RAN1#110b-e]
Agreement(FL proposal 3-2)
From RAN1 perspective, the following scenarios can be considered for Rel-18 L1/L2 mobility for beam indication timing. This will be updated depending on further RAN1 assessment and RAN2 decision on the time chart
  Scenario 1: Beam indication before cell switch command
  Scenario 2: Beam indication together with cell switch command
  Scenario 3: Beam indication after cell switch command
Interested companies are encouraged to further study the validity of the scenarios and the potential spec impact.
[Conclusion at RAN1#111]
Agreement
For beam indication timing for Rel-18 LTM,
  Support Scenario 2: Beam indication together with cell switch command,
    For Rel-17 unified TCI framework,
      Beam indication indicates TCI state for each target serving cell
  FFS: Scenario 1: Beam indication before cell switch command
  FFS: Scenario 3: Beam indication after cell switch command
FFS: Activation of TCI state(s) of target serving and/or candidate cell(s).
[Conclusion at RAN1#112]
Agreement
RAN1 shares the same understanding as RAN2 on agreement:
  The LTM mobility trigger information is conveyed in a MAC CE
The same MAC CE is used for the LTM triggering.
Agreement
The agreement on scenario 2 (Beam indication together with cell switch command) at RAN1#111 is further clarified as the following:
  Beam indication for the target cell(s) is conveyed in the MAC CE used for LTM triggering for scenario 2
[Conclusion at RAN1#112bis-e]
None
No open issue for this section

## Slide 25: Beam indication: Timing of beam indication – scenario 1 and/or 3
[Conclusion at RAN1#110b-e]
Agreement(FL proposal 3-2)
From RAN1 perspective, the following scenarios can be considered for Rel-18 L1/L2 mobility for beam indication timing. This will be updated depending on further RAN1 assessment and RAN2 decision on the time chart
  Scenario 1: Beam indication before cell switch command
  Scenario 2: Beam indication together with cell switch command
  Scenario 3: Beam indication after cell switch command
Interested companies are encouraged to further study the validity of the scenarios and the potential spec impact.
[Conclusion at RAN1#111]
Agreement
For beam indication timing for Rel-18 LTM,
  Support Scenario 2: Beam indication together with cell switch command,
    For Rel-17 unified TCI framework,
      Beam indication indicates TCI state for each target serving cell
  FFS: Scenario 1: Beam indication before cell switch command
  FFS: Scenario 3: Beam indication after cell switch command
FFS: Activation of TCI state(s) of target serving and/or candidate cell(s).
[Conclusion at RAN1#112]
Agreement
RAN1 shares the same understanding as RAN2 on agreement:
  The LTM mobility trigger information is conveyed in a MAC CE
The same MAC CE is used for the LTM triggering.
Agreement
The agreement on scenario 2 (Beam indication together with cell switch command) at RAN1#111 is further clarified as the following:
  Beam indication for the target cell(s) is conveyed in the MAC CE used for LTM triggering for scenario 2
[Conclusion at RAN1#112bis-e]
FL proposal was not agreed (this is further study proposal)
Companies are encouraged to further study the spec impact when Rel-17 ICBM and Rel-18 LTM can be operated simultaneously, e.g.
  TCI state pool for Rel-18 LTM can include or have any dependency of TCI states for Rel-17 ICBM operation
  UE capability
Conclusion
For scenario 3, it seems companies needs more time to think about the necessity of fallback operation. Thus, FL would like to close the discussion in this meeting, and come back at RAN1#113 based on the companies’ contribution.
Despite the concern on the simultaneous operation of Rel-17 ICBM and Rel-18 LTM, FL believes this discussion is necessary to complete Rel-18 LTM, at least from UE capability point of view
  The default is simultaneous operation of Rel-17 ICBM and Rel-18 LTM is allowed.
It is necessary to understand whether or not simultaneous operation of Rel-17 ICBM and Rel-18 LTM requires spec support
Discussion in RAN1#113 will be based on the contributions: urgent issues (if necessary) will be handled

## Slide 26: Beam application time: Beam application time
[Conclusion at RAN1#112bis-e]
Agreement
Companies are encouraged to study the beam application time for Rel-18 LTM, which may be different from that without serving cell change
  Definition of the beam application time
  The exact value(s), condition and UE capability
  Consider the interaction with the application of the candidate RRC configuration.
Discussion in RAN1#113 will be based on the contributions. However, the details can be discussed after all the necessary UE procedures have been decided

## Slide 27: Beam application time: Beam indication for multiple cells for CA
[Conclusion at RAN1#112bis-e]
The following FL proposal was postponed
For scenario 2, TCI state indication included in cell switch command indicates the TCI state(s) for SpCell of target cell(s)
For scenario 2, a TCI state indicated in the cell switch command is applied to multiple cells included in the list of simultaneous TCI state of the indicated target cell (when the list is configured) when the cells indicated in the list are active after cell switch command, i.e. the same mechanism as simultaneousU-TCI-UpdateList is reused for Rel-18 LTM
  FFS: when there are multiple (up to 4) simultaneousU-TCI-UpdateList configured for the [target candidate] cells.
  Note: RRC structures (i.e. under serving cell configuration or candidate cell configuration, etc) are up to RAN2
FL note: FL suggestion is to differ the approval until the introduction of TCI state activation is decided.
FL note: regarding the note “when the cells indicated in the list are active“, the intention of the proponent is that we should avoid the misunderstanding that this list and beam indication can be used to indicate the use of CA (and indication of SCells) after LTM. Hope this clarifies the intention
FL note:” [target candidate] cells.” FL believes this should be candidate cells as simultaneousU-TCI-UpdateList should be used in TCI state activation procedure.
Discussion in RAN1#113 will be based on the contributions
This proposal contains two aspects
  The cell to which the TCI state index(ies) in cell switch command applies
  How to apply beam indication to multiple target cells
Legacy approach (simultaneousU-TCI-UpdateList) assumes the presence of TCI state activation procedure, and TCI state activation has been agreed in RAN1#112bis-e
  Now we are ready to agree the FL proposal in RAN1#112bis-e
High Priority

## Slide 28: Beam indication: Open issues
Details of TCI state activation
  How many TCI states can be activated
  How to activate TCI states (by MAC CE?), and the information included in the MAC CE
Details of TCI state indication
  Which cell does “1 joint or 1 pair of UL and DL unified TCI State index” correspond to ?
  How to indicate TCI states for multiple target cells (CA case)
How TCI state pool for LTM is constructed
  Al1. 1: Extend existing TCI state pool to include candidate cell TCI states
    same approach as Rel-17 ICBM
  Alt.2: Introduce separate TCI state pool for LTM
    TCI state activation will also be separately performed for LTM and legacy BM
  Note: according to RAN2 assumption, TCI state pool for LTM may be managed separately from legacy TCI state pool
    Initial agreements, from RAN2 point of view (may be dep on RAN1 progress).
     RAN2 assumes that the location of configurations of TCI states for the candidate cells (used before/at cell switch) is external to the ServingCellConfig(s) of current serving cells and external to the configuration of the LTM candidate cells (same location as RS configuration).

## Slide 29: RAN1 agreements and FL plans for RAN1#112b-e
Cell switch command

## Slide 30: Cell switch command
[Conclusion at RAN1#110b-e]
Agreement(FL proposal 4-1)
Interested companies are encouraged to perform technical analysis of the cell switch command from a RAN1 point of view, e.g.
  Necessary information included in the command, which is relevant for RAN1 discussion
  Necessary number of bits for the information
  L1 impact or concern to use DCI or MAC CE for L1/L2 cell switch command
[Conclusion at RAN1#112bis-e]
Agreement
From RAN1 point of view, at least the following information can be included in the cell switch command, which is conveyed by MAC CE
  Information to identify the target cell(s)
    The details including bit number are designed by RAN2
  TA related information (details up to the discussion in A.I. 9.10.2)
  1 joint or 1 pair of UL and DL unified TCI State index for the target Cell
    Note: discussion on target SpCell is not precluded
  Active DL and UL BWPs for the target cell
  FFS: Triggering of aperiodic TRS transmitted from the target cell
  FFS: Triggering the CSI acquisition of the target cell and reporting to the target cell
  FFS: Triggering of aperiodic SRS transmission to the target cell
  FFS: C-RNTI
FFS: the presence of each field (i.e. always present or configurable)
Conclusion
Whether active DL and UL BWP of the target Cell/SpCell field, within the cell switch command, is always present or not is left to RAN2 decision.
Working Assumption
On the presence of beam indication within cell switch command, at least for scenario 2, following is supported:
A field to indicate 1 joint or 1 pair of UL and DL unified TCI State index for the target cell field is always present in the cell switch command.
Note: If scenarios 1 and 3 are agreed to be supported in R18 LTM other solutions may be considered.
Finalize the FFS parameters, e.g., whether FFS parameters in the previous agreement are needed in the cell switch command
Finalize which parameters should be always present vs configurable
Discussion in RAN1#113 will be based on the contributions.

## Slide 31: RAN1 agreements and FL plans for RAN1#112b-e
Preparation for LTM before reception of cell switch command

## Slide 32: Preparation for LTM: Details on DL synchronization to candidate cells
Continue the discussion on whether 2-step (SSB first and then TRS) or 1-step (Direct use of TRS) DL synchronization scheme should be supported for R18 LTM
  If no concussion is reached in RAN1#113 then RAN1 will not define specific DL synchronization steps, and this will be left to UE implementation
Check whether joint TCI state activation and beam indication in cell switch command (i.e., Alt 2) should also be supported
[Conclusion at RAN1#110b-e]
Agreement(FL proposal 5-1)
RAN1 to further study the potential RAN1 enhancements and spec impact to perform at least the following procedures prior to the reception of L1/L2 cell switch command aiming at the reduction of handover delay / interruption
  DL synchronization for candidate cell(s)
  TRS tracking for candidate cell(s)
  CSI acquisition for candidate cell(s)
  Activation/Selection of TCI states for candidate cell(s), if feasible
  Note: Uplink synchronization aspect will not be discussed under this A.I.
FFS: Whether the above procedures prior to the reception of L1/L2 cell switch command can be performed on candidate cell when it is deactivated SCell (if defined in RAN2)
[Conclusion at RAN1#111]
Agreement
Regarding the potential RAN1 enhancements to reduce the handover delay / interruption for Rel-18 LTM
  Support at least DL synchronization for candidate cell(s) based on at least SSB before cell switch command
    Further study the necessary mechanism, e.g. signaling and UE capability
[Conclusion at RAN1#112bis-e]
Agreement
For the Rel-17 unified TCI based beam indication in Rel-18 LTM, at least Alt 1 is supported:
Alt 1: TCI state activation of a candidate cell is received before the reception of beam indication of the candidate cell,
Alt 2: TCI state activation of a candidate cell is received together with the reception of beam indication of the candidate cell
  FFS: signalling details for TCI state indication, if both activation and indication are done in the same MAC CE message carrying switch command
Alt 3: Alt 1 and/or Alt 2 can be supported based on the UE capability
FFS: signalling details for TCI state activation
FFS: For Alt 1, whether/how TCI state activation for candidate cell(s) is allowed
Note: If scenarios 1 and 3 are to be supported other beam indication/TCI activation timing relationships are not precluded.
Discussion in RAN1#113 will be based on the contributions.

## Slide 33: Preparation for LTM: TRS tracking and CSI acquisition
Finalize whether TRS tracking and CSI acquisition on candidate cell before cell switch command should be supported in R18 LTM
  Needs to be finalized in RAN1#113
[Conclusion at RAN1#110b-e]
Agreement(FL proposal 5-1)
RAN1 to further study the potential RAN1 enhancements and spec impact to perform at least the following procedures prior to the reception of L1/L2 cell switch command aiming at the reduction of handover delay / interruption
  DL synchronization for candidate cell(s)
  TRS tracking for candidate cell(s)
  CSI acquisition for candidate cell(s)
  Activation/Selection of TCI states for candidate cell(s), if feasible
  Note: Uplink synchronization aspect will not be discussed under this A.I.
FFS: Whether the above procedures prior to the reception of L1/L2 cell switch command can be performed on candidate cell when it is deactivated SCell (if defined in RAN2)
[Conclusion at RAN1#111]
Agreement
Regarding the potential RAN1 enhancements to reduce the handover delay / interruption for Rel-18 LTM
  Support at least DL synchronization for candidate cell(s) based on at least SSB before cell switch command
    Further study the necessary mechanism, e.g. signaling and UE capability
[Conclusion at RAN1#112]
The following proposal was postponed
TRS tracking for candidate cells before the reception of cell switch command is supported
CSI acquisition for candidate before reception of cell switch command is supported
Discussion in RAN1#113 will be based on the contributions.

## Slide 34
Thank you