## Slide 1: Proposal on the calibration of the D2D simulation
KDDI
3GPP TSG RAN WG1 #73 R1-132717
Fukuoka, Japan
May 20th – 24th, 2013
Agenda item: 6.2.7.2
Document for Decision

## Slide 2: Proposed simulation assumption for calibration (1/3)
Property | General Scenario | PS Specific Scenario
Layout | [Option 3: Urban macro (500m ISD) -- all UEs outdoor] | [Option 5: Urban macro (1732m ISD)]
Carrier Frequency | 2GHz | 700 MHz
System bandwidth | 10MHz (FDD) | 10MHz
Network operation | 100% eNBs enabled | [100% eNBs enabled]
Network synchronization | all eNodeBs synchronized | 
UE mobility | [3] km/hr | [3] km/hr
UE RF parameters | Max Tx power of [31] dBm 1 Tx, 2 Rx antenna, Antenna gain 0 dBi, Noise figure 9 dB | 
UE inband emission mask | [not considered] | 
eNodeB RF parameters | As specified in [3GPP Case 1] | As specified in [3GPP Case 3]
Drop Distribution | According to the “uniform drop” in R1-131789 [1] | 
RAN1 performs a calibration campaign after fixing channel models.
As the first step, the following simulation parameters are used for the calibration of the channel model for UE-to-UE links.
It is FFS whether we need further calibration to confirm the UE dropping, in-band emission mask.
Asynchronous NW environment and out-of-coverage environment are the additional targets to do calibration. The exact parameters for such use cases are FFS.

## Slide 3: Proposed simulation assumption for calibration (2/3)
Non D2D traffic | D2D UEs don’t have non D2D (downlink & uplink) traffic.
Total number of active UEs per (active) cell | [10]
Channel model | FFS (decide after discussion over channel model assumption) or follow the Outdoor-to-Outdoor case without fast fading effect in Way forward R1-132502[2], i.e.) Pathloss: [ITU 1411-6 LOS and NLOS] LOS probability: [ITU-R IMT UMi] Shadowing: [7] dB log-normal
[1] Alcatel-Lucent and Alcatel-Lucent Shanghai Bell, “LTE D2D Dropping and association,” R1-131789.
[2] WF for D2D Channel Models, R1-132502.

## Slide 4: Proposed simulation assumption for calibration (3/3)
Additional assumption for calibration: option A Option A defines the case that uplink resources are shared between D2D UE and cellular UE.
Number of D2D UEs | [2] UEs/cell
Additional assumption for calibration: option B Option B defines the case that there are only D2D UEs in a certain band.
Number of D2D UEs | [10] UEs/cell
Depending on the assumption on the resource usage of D2D, we have the following options
for the additional assumption.
uplink scheduling method | Round robin (equal number of RBs are assigned among UEs)
D2D transmit power | fixed transmit power e.g.) [31] dBm
D2D scheduling method | Round robin (equal number of RBs are assigned among UEs)
Calibration metric | CDF curve of average IoT at D2D receivers
Traffic model for cellular and D2D UEs | [Full buffer]