## Slide 1: Suggestion on the PUCCH power control based on the offline discussion
LG Electronics
3GPP TSG RAN WG1 Meeting #73 R1-132801
Fukuoka, Japan, May 20-24
Agenda item: 6.1

## Slide 2: Background
In current TS36.213, it is unclear which PUCCH format UE should assume in PUCCH power control when it doesn’t transmit PUCCH but has received TPC for PUCCH by DCI format 1A/1B/1D/1/2A/2/2B/2C/2D .

## Slide 3: Suggestion
There are three alternatives discussed:
  Alt.1) UE follows reference PUCCH format as in case where TPC is received by DCI format 3/3A (as suggested in draft CR, R1-132217)
  Alt.2) UE follows PUCCH format which would be used if PUCCH was transmitted (as suggested in draft CR, R1-132800)
  Alt.3) No correction: UE behavior in this case is undefined
    UE behavior is undefined regarding which PUCCH format the UE should assume to accumulate TPC command for PUCCH received by DCI format 1A/1B/1D/1/2A/2/2B/2C/2D when the UE doesn’t transmit PUCCH
  For Rel-11, it is proposed to continue discussion in next meeting
  For Rel-10 and previous releases, UE behaviour in this case is undefined (alt.3)