## Slide 1: Way Forward on Small Cell Discovery
Broadcom, Qualcomm […], […]
R1-140979
3GPP TSG RAN WG1 #76
Prague, Czech Republic, 10th – 14th February 2014
Agenda item 7.2.4.2.2

## Slide 2: Agreements:
In the enhanced cell discovery procedure, UE can assume multiple signals are transmitted
  UE can assume transmission of PSS (identical to the Rel-8 waveform) at least for coarse time synchronization
  Which other signal(s) the UE can assume are transmitted is FFS
    Possible candidates are one or more instances of SSS, CRS, CSI-RS, and PRS
    Which signals are useful for which purpose is FFS
In addition to purposes given by the WID, cell multiplexing capability, UE power efficiency, and impact to legacy UE’s measurement can be considered when discussing candidate solutions
Rel-12 discovery procedure is configured only for RRC_CONNECTED UEs
FFS: Network assistance is provided to UEs for performing enhanced cell discovery. The information provided includes at least timing related information of discovery signal(s)

## Slide 3: Proposal
Define a discovery burst to include the signals in the Agreement
Occurrences of the discovery burst are time aligned between the OFF-cells to be measured belonging to the same frequency layer.
UE is informed of the timing of the bursts on a frequency layer
UE is configured one measurement pattern/discovery search window