## Slide 1: Way Forward on Small Cell On/off and Discovery Enhancements
Huawei, HiSilicon, NTT DOCOMO, Samsung, ZTE, Sony, Sharp, Hitachi, ETRI, Mediatek
R1-141868
3GPP TSG RAN WG1 #76bis
Shenzhen, China, 31th March – 4th April 2014
Agenda item 7.2.4.2

## Slide 2: Proposal
The Rel-12 enhanced discovery should enable cell/TP on/off operation in shared cell ID and non-shared cell ID scenarios
  TPs are identified by different TPIDs
The DRS enables the identification of TPID
  Scrambling ID(s) of the signal(s) transmitted in the DRS relate to TPID
    FFS whether/how PCID can also be identified from the scrambling ID(s) by the UE in shared cell ID scenarios
A TPID/PCID related list can be configured to a UE for the Rel-12 enhanced discovery
Rel-12 discovery based only on PSS/SSS/CRS with scrambling based on PCID is not sufficient
  CSI-RS is used for the Rel-12 discovery