## Slide 1
7.3.3.2 WF on simulation assumptions
3GPP TSG RAN WG1 #78bis R1-144444
Ljubljana, Slovenia, 6th – 10th October 2014
Nokia Networks, Nokia Corporation, CMCC, Samsung

## Slide 2: Simulation assumptions (phase 1 and phase 2)
Homogeneous scenarios | 3D-UMa ISD 500m, 3D-UMa ISD 200m with 41dBm Tx power (for 10MHz), 3D-UMi ISD 200m
Polarized antenna modeling | Model -2 from 36.873
Traffic model | Mandatory: FTP Model 1 with packet size 0.5 Mbytes (low ~20% RU*, medium ~50% RU, high ~70%RU), the number of UEs is variable and according to desired load for bursty Optional: Full buffer model
Wrapping method | Mandatory: Geographical distance based Optional: Radio distance based
Handover margin | 3dB
Metrics | Mean, 5%, 50% UPT
*RU clarification: multiple SU or MU layers are not counted multiple times towards RU, max RU=100%

## Slide 3: Simulation assumptions (phase 1 and phase 2)
System bandwidth | 10MHz (50 PRBs)
UE attachment | Option 1) Based on RSRP (formula) from CRS port 0*
Carrier Frequency | 2GHz
Network synchronization | Synchronized
UE Speed | 3km/h
UE distribution | according to 36.873
*This does not restrict any virtualization weights for CRS port 0

## Slide 4: Simulation assumptions (phase 1 and phase 2)
UE array orientation | ΩUT,a uniformly distributed on [0,360] degree, ΩUT,b = 90 degree, ΩUT,g = 0 degree
UE antenna pattern | Isotropic antenna gain pattern A’(θ’,ф’) = 1
Receiver | Non-ideal channel estimation and interference modeling, detailed guidelines according to Rel-12 [71-12] assumptions
 | LMMSE-IRC receiver, detailed guidelines according to Rel-12 [71-12] assumptions
UE Rx configuration | 2 Rx x-polar (+90/0)

## Slide 5: Simulation assumptions for phase-1
Feedback | PUSCH 3-2 for non-reciprocity operation (PUSCH 3-0 for reciprocity based operation)
 | CQI, PMI and RI reporting triggered per 5ms
 | Feedback delay is 5 ms
 | Rel-10 8Tx codebook based for non-reciprocity based operation (SRS for reciprocity based operation only for TDD)
Transmission scheme | TM10, single CSI process, dynamic SU/MU-MIMO with rank adaptation (no CoMP)
Overhead | 3 symbols for DL CCHs, 2 CRS ports and DM-RS with 12 REs per PRB
Scheduler | Frequency selective scheduling (multiple UEs per TTI allowed)
BS antenna configuration | antenna elements config: 8 x 4 x 2, TXRU config: 1 x 4 x 2
Number of UE transmit antennas | 1 or 2

## Slide 6: Simulation assumptions for phase 1
CSI-RS, CRS | CSI-RS 1-1 mapping to TXRU, only CRS port 0 is modeled for UE attachment, CRS port 0 is associated with the first column with +45 degree pol, CRS port 0 to TXRU mapping is given by [1, 0, 0, 0, 0, 0, 0, 0]
Downtilt | Antenna downtilting angle θetilt = [102] degree for 3D-UMa ISD 500m, 3D-UMi ISD 200m and θetilt = [106] degree for 3D-UMa ISD 200m
CSI-RS/SRS periodicity | 5 msec