## Slide 1: WF on Cell Association for HetNet Separate Frequency Band Scenario
NTT DOCOMO, CATT, CEWIT, CMCC, Ericsson, KDDI, LGE, NEC, Nokia Networks, Nokia Corporation, Samsung, Sony, ZTE
3GPP TSG RAN WG1 Meeting #80
Athens, Greece, 9th – 13th February 2015
Agenda item 7.2.4.1
R1-150791

## Slide 2: Background
Agreements from RAN1#79 and email discussion [79-06]:
  Use the following UE association method for HetNet scenario with separate frequency evaluations for Phase 1 evaluation:
    Geometry-based UE association with bias (i.e., RSRP of the target cell divided by the summation of RSRPs of all cells in the same frequency plus noise power for only simulation). Bias value is FFS.
    Tilting value for small cells and bias value are jointly determined with targeted small cell UE ratios of 2/3 for phase 1
It seems that we have two different interpretations on the highlighted part above:
  Alt. 1: from the word “geometry-based”
  Alt. 2: from the explanation in parenthesis
It is desired to determine the metric more explicitly to avoid different understandings among companies

## Slide 3: Proposal
  Use following UE association metric for phase 1 evaluation on HetNet scenario with separate frequency band:
  where T and RSRPi represent index of the target cell and RSRP from cell #i, respectively. The sum of the RSRP is taken over all cells in the same frequency band to the target cell.