## Slide 1: WF on PRACH CE Procedure
Huawei, HiSilicon, ALU, ASB, Ericsson, Intel, InterDigital, [Panasonic]
R1-150870
3GPP TSG RAN WG1 #80
Athens, Greece, February 9-13, 2015
Agenda item 7.2.1.2.3

## Slide 2: Rel-13 progress
The following agreements from Rel-12 were confirmed in RAN1#79:
RAN1 confirms that following PRACH related agreements in Rel-12 LC-MTC are applied for Rel-13 low-complexity UE
  For PRACH multiplexing scheme, CDM, and/or TDM and/or FDM are supported
  After the initial random access procedure, for a physical channel using repetition, the repetition level is up to network
  Multiple PRACH repetition levels are supported
  Repeating the existing preamble formats for PRACH enhancement
  In addition, define additional time/freq. resource region(s) separate for “enhanced coverage” UEs.
    Within new region, at least CDM is allowed.
  Specified maximum numbers of levels: Working assumption of 3 (this does not include “zero coverage extension”). More evidence needed if we were to extend this.
  eNB-configurable number of levels (1, 2, 3) up to specified max level.
1 attempt = configured number of repetitions.

## Slide 3: Rel-12 background
The following Rel-12 agreements are yet to be confirmed after RAN1#79:
Multiple PRACH repetition levels are supported (already in Rel-13)
  FFS: For initial random access, there is one to one mapping between PRACH repetition level and PRACH resource set. UE selects a PRACH repetition level and transmits the PRACH preamble using the PRACH resource set according to the selected PRACH repetition level
  FFS: details of PRACH resource set, repetition levels
  FFS: details of random access procedure including initial selection for repetition level
Number of repetitions per level:
  FFS for configurable value.
  FFS ranges of this value per level – come back later in week.
FFS: Power ramping is supported
If UE does not receive a RAR after 1 attempt, it moves to next highest level (e.g. 5 to 10, and 10 to 15).
At highest level, FFS on how many attempts are allowed, and the overall procedure (e.g. Backoff etc).
Possible agreements from Rel-12 yet to be considered after RAN1#79:
Starting level for contention based random access procedure:
  Case 1: FFS between starting at the lowest level or defining it based on measurement or based on other ways
  Case 2: working assumption: In RRC connected mode could be configured by eNB (dedicated RRC signalling).

## Slide 4: Proposals
For coverage enh of PRACH , for initial random access
  There is one to one mapping between PRACH repetition level and PRACH resource set
  WA: UE selects a starting PRACH repetition level based on DL measurement(s) and transmits the PRACH preamble if the DL measurement is reliable
    FFS details of the DL measurement(s)
    FFS which level is selected if the DL measurement(s) is/are unreliable
    WA subject to RAN4 feedback on measurement reliability and time
The eNB can configure how many attempts are allowed for each PRACH repetition level
FFS: Power ramping or always max power used within each repetition level
If UE does not receive a RAR after the allowed number of attempts, it moves to the next higher repetition level
FFS UE behavior when UE receives RAR, but fails contention resolution

## Slide 5: Proposals
FFS how/if to use measurements to decide whether PRACH CE is needed or not
When CE is needed, for coverage enh of PRACH, for initial random access
  There is one to one mapping between PRACH repetition level and PRACH resource set
  WA: UE selects a starting PRACH repetition level based on DL measurement(s) and transmits the PRACH preamble if the DL measurement is reliable
    FFS details of the DL measurement(s)
    FFS which level is selected if the DL measurement(s) is/are unreliable
    WA subject to RAN4 feedback on measurement reliability and time
The eNB can configure how many attempts are allowed for each PRACH repetition level
FFS: Power ramping or always max power used within each repetition level
If UE does not receive a RAR after the allowed number of attempts, it moves to the next higher repetition level
FFS UE behavior when UE receives RAR, but fails contention resolution