## Slide 1: WF on Requirement & functionalities for LAA UL Transmission
ZTE …
R1-150893
3GPP TSG RAN WG1 #80
Athens, Greece, 9th – 13th February 2015
Agenda item 7.2.3.3

## Slide 2: Background
In RAN1_80, many contributions raised the following issues regarding UL transmission for LAA
  eNB side CCA alone could lead to various potential issues such as hidden nodes problem , lower spectrum efficiency etc
  Synchronous UL HARQ operation in LAA will not be guaranteed, more flexible scheduling mechanism should be considered.
  SRS should be supported
According to ETSI regulation, the occupied channel bandwidth, shall be at least 80% of the declared Nominal Channel Bandwidth.
  However, how to satisfied the 80% requirement is not clear and some interpretation could result in significant system spectrum efficiency loss

## Slide 3: Proposal
Consider at least the following functionalities for LAA UL transmission if UL on unlicensed carrier is supported and captured in the TR
  UE side CCA
  Asynchronous HARQ
  SRS
Consider the following clarification to meet the requirement Occupied Channel Bandwidth for UL transmission
  Define the Nominal Channel Bandwidth to be the minimum bandwidth of 5MHz and consider a 20MHz system bandwidth as four adjacent channels
  Signal in the definition for the Occupied Channel Bandwidth could come from multiple UEs