## Slide 1: Handling of power reservation for non-overlapped transmission in PCM2
Huawei, HiSilicon
3GPP TSG RAN WG1 #80
Athens, Greece, Feb, 9 – 13, 2015
Agenda item 7.1
R1-150934

## Slide 2: Background(1/2)
It was agreed in RAN1#77 that
Reserve P_SeNB and/or P_MeNB towards each eNB if there is potential uplink transmission
  If the UE knows it does not have transmission in the other CG in overlapped subframes based on at least semi-static information (e.g., TDD UL/DL config.), UE does not reserve the power for that CG
It was addressed in 36.213 as follows:
  If the UE determines based on higher layer signalling that transmission(s) on CG1 in subframe do not overlap with UE transmission(s) on other CG, then the UE shall use , where is the linear value of the UE total configured maximum output power (defined in [6]) in subframe i.
There is concern that eNB cannot have common understanding with the UE about the higher layer signaling that UE utilized

## Slide 3: Background (2/2)
In the definition of Pcmax for dual connectivity in 36.101, the following is addressed for unsynchronized overlapping transmission
if MCG leads, the (p,q) and (p,q-1) pairs are considered for PCMAX definition i.e. for deriving the values of PCMAX_L and PCMAX_H .
if SCG leads, the (p-1,q) and (p,q) pairs are considered for PCMAX definition i.e. for deriving the values of PCMAX_L and PCMAX_H .
It could mean that it is assumed that UE has decoded (E)PDCCH in subframe q when the UE derives the Pcmax of subframe p in case 1 , and UE has decoded (E)PDCCH in subframe p when the UE derives the Pcmax of subframe q in case 2. Therefore UE knows it does not have transmission in the other CG in overlapped subframes based on (E)PDCCH decoding

## Slide 4: Proposal
Address the agreement after the power allocation formula,
such that the reserved power for CG2 can be set to zero
Send LS to RAN4 to clarify the understanding whether (E)PDCCH decoding has to be processed when deriving Pcmax. Continue discussion on whether and how to revise ‘based on higher layer signaling’ depending on the reply from RAN4.