## Slide 1: Proposal on CSI for LAA
Huawei, Ericsson
3GPP TSG RAN WG1 Meeting #80bis R1-152285
Belgrade, Serbia, 20th - 24th April 2015
Agenda item: 7.2.4.2
Document for decision

## Slide 2: Proposal
For TM10
  NZP CSI-RS transmission is subject to LBT
  The UE cannot assume that CSI-RS and CSI-IM are transmitted periodically
  Signaling from eNB indicates to UEs when NZP CSI-RS can be assumed to be present in a subframe
  Signaling from eNB indicates to UEs when CSI-IM can be assumed to be present in a subframe
  Further discuss the possible methods for signaling

## Slide 3: Proposal
For the CSI relative to an LAA SCell
  CSI reporting for an LAA cell is aperiodic
  Aperiodic CSI can be reported on PUSCH transmitted on an LAA Scell
    Aperiodic CSI can also be reported on a licensed carrier
  Further discuss whether periodic CSI reporting needs to be supported, and the definition of the CSI reference resource for periodic CSI reporting