## Slide 1: WF on Extending CQI Table for MTC
Ericsson, MediaTek, Panasonic, NTT DoCoMo
3GPP TSG RAN WG1 Meeting #80is R1-152368
Belgrade, Serbia, April 20-24, 2015
Agenda item 7.2.1.1

## Slide 2: Background (1)
Agreements from RAN1#80:
  For UEs in enhanced coverage:
    Repetition/bundling of PDSCH across multiple subframes is supported
      Multiple repetition/bundling levels in time domain are supported
    Repetition/bundling of ‘physical channel(s) carrying UL data’ is supported
      Multiple repetition/bundling levels in time domain are supported

## Slide 3: Background (2)
CQI index | modulation | code rate x 1024 | efficiency
0 | out of range |  | 
1 | QPSK | 78 | 0.1523
2 | QPSK | 120 | 0.2344
3 | QPSK | 193 | 0.377
4 | QPSK | 308 | 0.6016
5 | QPSK | 449 | 0.877
6 | QPSK | 602 | 1.1758
7 | 16QAM | 378 | 1.4766
8 | 16QAM | 490 | 1.9141
9 | 16QAM | 616 | 2.4063
10 | 64QAM | 466 | 2.7305
11 | 64QAM | 567 | 3.3223
12 | 64QAM | 666 | 3.9023
13 | 64QAM | 772 | 4.5234
14 | 64QAM | 873 | 5.1152
15 | 64QAM | 948 | 5.5547
4-bit CQI Table (TS36.213 V12.4.0, Table 7.2.3-1)

## Slide 4: Proposal
Existing CQI table is extended with new CQI entries for LC/CE UEs.
The new CQI entries are defined to support repetition/bundling across multiple subframes
FFS: details of new CQI entries
FFS: 64-QAM, 16-QAM entries in existing CQI table are removed
FFS: impact to MCS table