## Slide 1: Way forward on Link to System Modeling for MUST evaluation
Huawei, HiSilicon, MediaTek, Qualcomm, Nvidia, Intel, CATR
3GPP TSG RAN WG1 Meeting #81 R1-152394
Belgrade, Serbia, 20th – 24th April 2015
Agenda Item: 7.2.7.2

## Slide 2: Proposal for L2S modeling
Companies should present their L2S modeling when providing system simulation results.
Companies are encouraged to provide link-level simulation results validating the used L2S model(s).
Examples are attached for reference in following slides, which does not preclude other examples of L2S modeling.
Note: Applicability of these L2S modeling examples needs to be verified for the MUST case.

## Slide 3: Example for L2S modeling –for Far UE
For the far UE, the signal of near UE is treated as noise, so the L2S modeling for far UE is straightforward by reusing conventional pre Rel-13 model(s).

## Slide 4: Examples for L2S modeling – near UE-1
An L2S modeling for CWIC receiver is:
  when the decoding for the data layer of far UE is successful, the cancellation of this data layer is assumed.
    The modeling of the residual interference and impairments are required
  when the decoding for the data layer of far UE is unsuccessful, there are two options for modeling,
    a) no cancellation of this layer, decoding for the layer of near UE fails;
    b) reuse models of receivers from conventional non-MUST schemes, e.g. CWIC or SLIC of NAICS.

## Slide 5: Examples for L2S modeling -near UE- 2
An L2S modeling for ML/R-ML receiver is:
  With revised lower-bound and upper-bound SNR, reuse the modeling methodologies of ML/R-ML of NAICS

## Slide 6: Examples for L2S modeling- near UE- 3
An L2S modeling for SLIC receiver is:
  reuse the modeling methodologies of SLIC of NAICS