## Slide 1: WF on EPDCCH Decoding Candidates for MTC
Ericsson, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, InterDigital, MediaTek, Panasonic, Samsung, Sony, ZTE
3GPP TSG RAN WG1 Meeting #80is R1-152405
Belgrade, Serbia, April 20-24, 2015
Agenda item 7.2.1.1

## Slide 2: Background
Rel-12 RAN1#76 Agreement:
  At least for unicast traffic: Study tradeoff and performance of the following options:
      Option 1: single (E)CCE aggregation level and multiple repetition levels
      Option 2: multiple (E)CCE aggregation levels and single repetition level
      Option 3: multiple (E)CCE aggregation levels and multiple repetition levels
      Examples of the options can be found in R1-141030
RAN1#79 agreement:
  At least for unicast channel,
    For the ‘Physical downlink control channel for MTC’ for Rel-13 low complexity UEs and UEs in enhanced coverage,
      UE monitoring of multiple ‘Physical downlink control channel for MTC’ decoding candidates and/or one or more repetition level(s) is supported at least for the UE-specific search space
RAN1#80 agreement:
  For UEs in enhanced coverage:
    Repetition across multiple subframes is supported for the ‘Physical downlink control channel for MTC’
      Multiple repetition levels in time domain are supported

## Slide 3: Proposal
Multiple ECCE aggregation levels and multiple numbers of repetitions are defined in specification for ‘Physical downlink control channel for MTC’
A set of possible combinations of {ECCE aggregation level, number of repetition} is defined in the spec
A subset of all possible combinations of {ECCE aggregation level, number of repetitions} can be semi-statically configured for constructing a UE-specific search space for ‘Physical downlink control channel for MTC’ by higher-layer signaling
  If configured by higher-layer signaling, it is FFS whether signaling is implicit or explicit.
  Parameters defining an ‘Physical downlink control channel for MTC’ blind decoding candidate in a UE-specific search space (USS) include at least an ECCE aggregation level, a number of repetitions and a starting ECCE index