## Slide 1: WF on CW adjustment
Ericsson, Broadcom
3GPP TSG RAN WG1 #82 R1-154791
Beijing, China
24th – 28th August 2015
Agenda item: 7.2.4.1
Document for decision

## Slide 2: Background
Agreements:
For LBT Category 4 operation for PDSCH, following approaches for CWS (contention window size) adjustment should be captured in TR.
  Option 1: based on feedback/report of UE(s) (e.g. HARQ ACK/NACK)
  Option 2: based on eNB’s assessment (e.g. sensing based adjustment)
  Note: combination of those options are not precluded.

## Slide 3: Background
802.11 contention window (CW) is doubled if ACK frame is not received by the transmitter
A-MPDU and Block ACK protocols in 802.11n and 802.11ac
  A-MPDU and Block ACK protocols were introduced to improve MAC throughputs
  CW is not doubled as long as the BlockACK frame is received successfully by the transmitter
    Even if the Data Blocks are not received successfully by the receiver
Data
Data
Data
Data
BA
Data
Data
Data
BAR
BA

## Slide 4: Proposal
For LBT Category 4 operation for PDSCH, the CWS (contention window size) is adjusted based on HARQ ACK/NACK feedback.
  FFS on the details of how to use the HARQ ACK/NACK feedback