## Slide 1: WF on LAA DRS design and transmission timing
NTT DOCOMO, Panasonic, Samsung, Huawei, Sharp
R1-154817
3GPP TSG RAN WG1 Meeting #82
Beijing, China, 24th – 28th August 2015
Agenda item 7.2.4.2.1

## Slide 2: Background
During LAA SI, following agreements were made.
  DRS design should allow DRS transmission on an LAA SCell to be subject to LBT
  Consider the following 2 options for the transmission of DRS within a DMTC window if LBT is applied to DRS
    Alt1: Subjected to LBT, DRS is transmitted in fixed time position within the configured DMTC
    Alt2: Subject to LBT, allow the DRS to be transmitted in at least one of different time positions within the configured DMTC
      Note: The number of different time positions should be restricted
      Note: One possibility is one time position in the subframe
    Modifications to Rel-12 DMTC configuration are FFS
  Note: this does not preclude the possibility to allow other DRS transmissions outside of the configured DMTC
According to evaluation results in R1-154264 and R1-154767, it is observed that the DRS transmission probability of Alt.2 is much higher than that of Alt.1

## Slide 3: Proposal
Subject to LBT, allow the DRS to be transmitted in at least one of different time positions within the configured DMTC
  DRS occasion duration which doesn’t include potential initial signal part is less than 1 ms
  DRS occasion contains at least PSS/SSS/CRS and is time-continuous
  Allow DRS transmission in subframe other than #0 and #5
  Following alternatives can be considered to solve sequence generation issue for SSS/RS in subframe other than #0/#5
    Alt. 1: Generate SSS/RS sequences according to the subframe index of DRS and UE identifies the subframe index of DRS by the sequence.
    Alt. 2: Generate SSS/RS sequences irrespective of the subframe index of DRS and UE doesn’t need to identify the subframe index of DRS for RRM measurement.
    Alt. 3: Generate SSS/RS sequences irrespective of the subframe index of DRS and UE identifies the subframe index of DRS by signaled information in DRS.