## Slide 1: WF on frequency hopping patterns for MTC
Ericsson, NEC, NTT DoCoMo, Sony
R1-154824
3GPP TSG RAN WG1 Meeting #82
Beijing, China, 24th - 28th August 2015
Agenda item 7.2.1.1

## Slide 2: Proposal
Frequency hopping (when enabled) occurs between two or four (FFS) narrowbands.
  FFS signaling is via (a) semi-static or (b) dynamic indication of predefined pattern
Frequency hopping pattern period Y (ms) is selected between two options:
  Option 1: Y is based on (half) radio frames, e.g. Y = {5, 10, 20} ms
  Option 2: Y is based on powers of 2, e.g., Y = {4, 8, 16} ms
  FFS how to define Y to account for invalid subframes including TDD configurations and MBSFN subframes
  FFS whether frequency hopping period Y is configurable by the network or not
The frequency hopping period for MTC-SIB1 is fixed in specification.
Consider cell-id-based randomization of the two narrowbands at least for common messages (SIB/RAR/Paging).