## Slide 1: WF on CSI Measurement Restriction
Samsung, Ericsson, CATT, NTT DOCOMO, KT, CMCC, ZTE, LG
3GPP TSG-RAN WG1#82 R1-154924
Beijing, China, August 24-28,2015
Agenda Item: 7.2.5.1.2

## Slide 2: Definition of CSI Measurement Restriction(MR)
For a given CSI process/CSI-RS resource, MR on channel measurement is ON when channel used for CSI computation can be estimated from X NZP CSI-RS subframe(s) up until and including CSI reference resource
  Channel measurement is derived from NZP CSI-RS
For a given CSI process, MR on interference measurement is ON when interference used for CSI computation can be estimated from Y CSI-IM subframe(s) up until and including CSI reference resource
  Interference measurement is derived from CSI-IM
For a given CSI process/CSI-RS resource, MR may be higher-layer configured for both channel and interference
  MR for channel and interference can be configured independently
Note: Channel and interference MR are considered independently

## Slide 3: Possible CSI MR Configurations
Alt.1: Fixed MR ON or OFF via higher-layer configuration
  X/Y are fixed to a single value respectively in specification
Alt.2: Configurable MR ON or OFF via higher-layer configuration
  X={OFF, 1, … , NX} are higher-layer configurable
  Y={OFF, 1, … , NY} are higher-layer configurable
Alt.3: CSI measurement is periodically reset
  Reset period and subframe offset are higher-layer configured
  Note: X/Y are not configured

## Slide 4: Illustration
Possible CSI MR configurations:
  Alt.1 & 2:
  Alt.3:
subframe
CSI reference resource
Averaging window, X/Y
NZP CSI-RS
/ CSI-IM
…
…
…
subframe
CSI reference resource
Averaging window, X/Y
…
…
NZP CSI-RS
/ CSI-IM

## Slide 5: Action needed for RAN1#82b
Necessity for channel MR is decided via email discussion by 9/22
  Note: Needs for channel and interference MR are considered independently
Select one of the alternatives for each of CSI-RS and/or CSI-IM on previous slides
Decide if CSI measurement restriction can be configured (ON or OFF) for CSI reporting class A
Decide if CSI measurement restriction can be configured (ON or OFF) for CSI reporting class B
FFS: application of CSI MR for aperiodic CSI reporting, e.g., MR based on L1 triggering and/or higher-layer signaling for dynamic CSI request.