## Slide 1: WF on ED adaptation
Ericsson, Qualcomm
3GPP TSG RAN WG1 #82 R1-154970
Beijing, China
24th – 28th August 2015
Agenda item: 7.2.4.1
Document for decision

## Slide 2: Background
TR 36.889 recommends the following:
  For LAA, it is recommended that LAA supports a mechanism to adaptively change the energy detection threshold, at least for the downlink, i.e., it is recommended that LAA support a mechanism to adaptively lower the energy detection threshold from an upper bound. Such an adaptation mechanism does not preclude static or semi-static setting of the threshold. It should be noted that such a mechanism to adaptively lower the threshold may or may not have specification impact.

## Slide 3: Proposal
When performing energy detection, the eNB energy detection threshold should be adapted to ensure good coexistence with other operators and other technologies
Coexistence can be checked by testing
  FFS: Tests to check coexistence
The chosen semi-static maximum allowed energy detection threshold shall be signaled by the eNB in each DRS occasion