## Slide 1: Way Forward on P-CSI dropping
NTT DOCOMO, INC.
R1-154992
3GPP TSG RAN WG1 #82
Beijing, China, 24th – 28th August 2015
Agenda item 7.2.2.1.2

## Slide 2: Following is still under discussion
Possible agreements:
Define dropping rules for periodic CSI reporting on PUCCH and/or PUSCH
  FFS: how and whether to achieve a common understanding between eNB and UE

## Slide 3: Background
If UE is power-limited when transmitting multi-cell P-CSI (+ HARQ-ACK/SR),
  If the power-scaling/dropping is applied to PUCCH or PUSCH, the whole UCI may not be correctly received
  If the UE is allowed to drop some/all of the P-CSI, the remaining UCI may be correctly received
However, if UE is allowed to drop some/all of the P-CSI,
  Common understanding b/w eNB and UE may not be achieved
  eNB needs to check blindly how many and which P-CSIs are reported

## Slide 4: Proposal 1
For the UE configured with Rel.13 CA configurations, one of the following is agreed:
  Alt.1: Define dropping rules for periodic CSI reporting on PUCCH and/or PUSCH
    Any P-CSI dropping event is based on the information known by the eNB
  Alt.2: Define dropping rules for periodic CSI reporting on PUCCH and/or PUSCH
    UE is allowed to drop P-CSI based on the information not known by the eNB

## Slide 5: Proposal 2
If the P-CSI dropping rules for Rel.13 CA configurations is defined, it is based on the priorities that are already specified in Rel.8-12, i.e., based on the following:
  PUCCH reporting type
  CSI process ID
  CSI subframe set
  ServCellIndex