## Slide 1: Draft WF on PBCH repetition for enhanced frequency tracking
Qualcomm, Panasonic, Samsung, Intel, ZTE
R1-156192
3GPP TSG RAN WG1 Meeting #82bis
Malmo, Sweden, 5th - 9th August 2015
Agenda item 7.2.1.6

## Slide 2: Background
In low SNR operation, it might be difficult to obtain a good frequency error estimation
The following working assumption was introduced in RAN1#82:
  Consider mapping PBCH repetition symbols for improving frequency tracking loop operation
    FFS detailed mapping (within and across subframes)
This repetition scheme allows to use the PBCH data tones for frequency tracking before decoding PBCH

## Slide 3: Proposal
Confirm working assumption of PBCH repetition for enhanced frequency tracking.
Symbols without CRS are repeated in symbols without CRS
Symbols with CRS may be repeated:
  In symbols with CRS
  In symbols without CRS, where the PBCH repetition is not mapped to the tones corresponding to CRS
FFS: More detailed mapping