## Slide 1: WF on design principles of resource allocation in PC5-based V2V
Ericsson
R1-156205
AI 7.2.8.2.1

## Slide 2: Proposal for working assumption
The following design principles may be considered for RA in V2V-PC5:
  The eNB may control the resources used for transmission on a carrier:
    Exact resources for transmission
    Set of resources for autonomous selection by the UE
    FFS: other transmission parameters controlled by eNB
    FSS: how the eNB acquires information for RA, including signaling from UEs
  The UE may be RRC pre-configured for operation when out of coverage on the carrier used for PC5 V2V

## Slide 3: Proposal for working assumption
  Each V2V data transmission is scheduled by a sidelink SA
    FFS whether SA and Data are transmitted on separate physical channels:
      In case of different channels, are SA and data transmitted on separate pools
    FFS which pool(s) are monitored by a UE
    FFS which pool(s) are used for transmission by a UE for a given TB

## Slide 4: Proposal for working assumption
  A single SA may schedule multiple transmissions of a given TB
    FFS details about number of retransmissions (if any), MCS, resources and RV used by each transmission
  A single SA may schedule multiple TBs
    FFS details of resources and other transmission parameters used for each TB

## Slide 5: Proposal for working assumption
  UE autonomous RA can be improved by one or more of the following means:
    Randomization of resources used for different transmissions
    Collision avoidance:
      A UE identifies the resources that will be occupied by the other UEs and avoids a colliding resource allocation for its transmission.
    Resource partitioning between different transmissions:
      FFS which type of information is used for partitioning
    FFS whether SA and data RA are independent or not
    FFS: which of the above technique(s) are supported

## Slide 6: Proposal for working assumption
  SA and data patterns:
    Both SA and data transmissions occur using one of multiple supported resource patterns
    SA indicates resource pattern for data
    FFS: how to design the patterns