## Slide 1
Detailed design for multi-PRB PF3
Huawei, HiSilicon,CMCC
R1-156306
3GPP TSG RAN WG1 #82bis
Malmo, Sweden, 5th – 9th October 2015
Agenda item 7.2.2.1.1

## Slide 2
  As data rate and DL carriers increase, number of UEs configured with PF3 may not be small
    For CA scenario #4, one UL carrier can carry many PF3 resources from UEs
  The case of moderate payloads is more common than large HARQ-ACK payloads
    New CDF format multiplexing with PF3 saves UL overhead
      More flexibility for PUCCH RA
      Note: The analysis can be refer to R1-155091
Motivation

## Slide 3
  A single DFT operation is used
  The relation among the resource index (values from 0-549) and the OCC index can reuse the design of PF3
  Multiplexing with legacy PF3
    Considering the symbol-level frequency cyclic shifting, and to maintain the orthogonality with PF3,
      K times of cell-specific shifts for data symbols of PF3 should be used, wherein K is the number of PRBs per slot (Note that the details can refer to R1-155091)
      The original formula is changed to
Design for multi-PRB PF3 – data symbol

## Slide 4
  For PF3, the resource index is mapped to DMRS shift, which should be kept for multi-PRB PF3
  Alt 1:concatenating PF3 length-12 DMRS sequences
    The PAPR could be reduced by using different DMRS cyclic shifts for different PRBs
      Note: The PAPR results can be found in R1-155091
  Alt2:Using a single K*12 length DMRS sequence, wherein K is the number of PRBs per slot
Design for multi-PRB PF3 – RS symbol

## Slide 5
  The resource index is the same as PF3, values from 0-549
    Resource allocation reuses ARI
    Format adaptation can be discussed further
  The number of PRBs per slot: [2-4]
    No RRC parameter is needed if only one value is selected.
  Cell-specific cyclic shifts for data symbols
    Update the formula in 36.211
  Indication for different DMRS cyclic shifts among different PRBs
Spec impact