## Slide 1: WF on Agenda 7.2.1.6
Nokia Networks
R1-156324
3GPP TSG RAN WG1 #82bis
Malmö, Sweden, 5th - 9th October, 2015
Agenda item 7.2.1.6

## Slide 2: Proposals on PBCH repetition
Confirm working assumption of PBCH repetition for enhanced frequency tracking.
Symbols without CRS are repeated in symbols without CRS
Symbols with CRS may be repeated:
  In symbols with CRS
  In symbols without CRS, where the PBCH repetition is not mapped to the tones corresponding to CRS
FFS: More detailed mapping
Qualcomm, Panasonic, Samsung, Intel, ZTE, ALU, LGE, Sony

## Slide 3: Proposals on SI Acquisition Across Windows
Acquisition of SI messages across SI windows is feasible in idle mode
The maximum number of SI messages that can be acquired across SI windows is FFS
Nokia Networks, Intel, Alcatel Lucent, Sony, Panasonic, Sierra Wireless, CATT, Samsung, ZTE, NTT DoCoMo, Ericsson, InterDigital, MediaTek, Huawei, HiSilicon, LGE

## Slide 4: Proposals on SIB1bis (1)
SIB1bis is transmitted periodically with a period of TSIB1bis radio frames
  Within a period, SIB1bis can be repeated a number of times
  RV cycling {0,2,3,1,…} is used for each SIB1bis transmission within a period
SIB1bis content does not change over X*TSIB1bis radio frames
SIB1bis transmission period TSIB1bis is predefined
  TSIB1bis = [8] radio frames
Repetition number RSIB1bis within a period is derived from MIB
Nokia Networks, Ericsson, Samsung, Panasonic, NEC, LGE, Intel, InterDigital, CATT, Sierra Wireless, MediaTek, NTT DoCoMo, ZTE, Sony, Alcatel Lucent

## Slide 5: Proposals on SIB1bis (2)
Time location is determined by
  Option 1:
    Time location is determined from RSIB1bis, PCID and SFN
  Option 2:
    Time location is determined from RSIB1bis and PCID
  Option 3:
    First transmission of SIB1bis is transmitted in subframe #5 of radio frames for which the SFN mod TSIB1bis = 1
    Time location for repetitions is determined from RSIB1bis
Nokia Networks, Ericsson, Samsung, Panasonic, NEC, LGE, Intel, InterDigital, CATT, Sierra Wireless, MediaTek, NTT DoCoMo, ZTE, Sony, Alcatel Lucent

## Slide 6: Proposals on SIB1bis (3)
For TDD, subframes #1 and #6 are not used for SIB1bis transmission
Nokia Networks, Ericsson, Samsung, Panasonic, NEC, LGE, Intel, InterDigital, CATT, Sierra Wireless, MediaTek, NTT DoCoMo, ZTE, Alcatel Lucent

## Slide 7: Proposal on CFI
Confirm the Working Assumption with revised description of the same:
  For subframes containing PDSCH carrying SIB1bis, the starting OFDM symbol of SIB1bis reception is a fixed value predefined in the specification
    The fixed value is equal to the maximum CFI value for the given system configuration (TDD/FDD, system bandwidth)
  For M-PDCCH and other PDSCH, the starting OFDM symbol is broadcast to all low-complexity/coverage-enhancement UEs in a cell via a shared higher layer parameter in SIB1bis
    The higher layer parameter is a 2-bit field, indicating starting OFDM symbol  {1,2,3} for N_RB^DL >10 , and  {2,3,4} for N_RB^DL 10
    As in existing system, the starting OFDM symbol for subframe 1 and 6 for TDD is maximum 2
4-th value signaled by the 2-bit field indicates: starting OFDM symbol =0
Ericsson, LG, Intel, Samsung, Sony, DoCoMo, Nokia Networks, Sierra Wireless, MediaTek, Panasonic, NEC, ZTE, CATT, Alcatel Lucent