## Slide 1: WF on LAA DL Multi-Channel LBT ED Threshold
Broadcom Corporation, CableLabs, Cisco Systems, Ruckuswireless
3GPP TSG RAN WG1 #83 R1-157631
Anaheim, USA
15th –22th November 2015
Agenda item: 6.2.3.1
Document for decision

## Slide 2: Background
Wi-Fi 11ac CCA sensitivity for secondary channels
  A valid 40MHz OFDM PPDU at or above –72dBm with > 90% probability within 25 µs.
  Most 11ac devices implement the ED with threshold -75dBm on 20MHz channel to meet the requirement
From Wi-Fi specification evolution from 11n to 11ac, large benefits of coexistence were observed from reducing the CCA threshold from -62dBm to -72dBm on the secondary channels
  11n only requires CCA threshold -62dBm on secondary 20MHz channel

## Slide 3: Proposal
If the LAA eNB is not aware of the absence of Wi-Fi devices on the set of channel (s) that it intends to transmit,
  Max ED threshold on channel (s) on which Cat-4 LBT is employed shall equal the same threshold as that used for single channel transmission
  Max ED threshold on channel (s) on which Cat-4 LBT is not employed shall equal -75 dBm