## Slide 1: WF on ED Threshold for LAA Frequency Reuse
Samsung, [ZTE], [Huawei]
R1-157644
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th – 22nd November 2015
Agenda item 6.2.3.1

## Slide 2: Background
We have the following agreements about frequency reuse support
At least the following options can be further studied to enable improved freq. reuse for LBE for DL LAA.
  CCA threshold adaptation
  TX start timing alignment
  Signal subtraction from ED or modified ED (excluded from Rel-13 @ RAN1#82)
  Combinations of those options or other alternatives are not precluded

## Slide 3: Proposal (1/2)
The following ED threshold adaptation should be applied at eNB,
  If the eNB detects the presence of WiFi, the eNB uses maximum ED threshold 1 (Th1)
  Else, if the eNB identifies the presence of inter-operator LAA interference, the eNB uses maximum ED threshold 2 (Th2)
  Else the eNB uses maximum ED threhold 3 (Th3)
Note: Th1>Th2≥Th3

## Slide 4: Proposal (2/2)
How to identify the presence of inter-operator LAA interference:
  Baseline: by monitoring muted REs in the initial signal
  Addition: by monitoring muted REs in the PDSCH
  Note on specification impact: The baseline needs a restriction of leaving some REs blank on initial(reservation) signal transmission