## Slide 1: WF on PDSCH, PUSCH and PUCCH Number of Repetitions RRC Values for eMTC
Sony, [Ericsson, Sierra Wireless, IDC…]
R1-157674
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda item 6.2.1.6

## Slide 2: Background
The repetition levels for M-PDCCH were agreed earlier in RAN1#83:
Proposals for repetition levels for PUCCH and PRACH are contained in respective WFs on PUCCH and PRACH
The email discussion [82b-01] on RRC parameters for MTC identified that the values for “Set of PDSCH / PUSCH repetition numbers” are FFS
This WF proposes repetition numbers for PDSCH and PUSCH

## Slide 3: Proposal on Number of HARQ Processes for Small Coverage Enhancements
Background
RAN1#82 agreement:
For HD-FDD, FD-FDD and TDD, if the UE is operating with no repetition, the same max number of DL and UL HARQ processes as for Cat-0 UE in Rel-12, except that:
  FFS if the number of DL HARQ processes should be increased for TDD with respect to that of Rel-8 for the case of no repetition
FFS the case of small coverage enhancement
Soft buffer management is based on a maximum of 8 DL HARQ processes as in Rel-8
Proposal
For FDD, if the UE is operating in Mode A
  UE is expected to support no more than N=8 DL HARQ processes to receive unicast PDSCH
  UE is expected to support no more than N=8 UL HARQ processes to transmit unicast PUSCH

## Slide 4: Proposal: Set of PDSCH/PUSCH Repetition Numbers
The predefined set of PDSCH/PUSCH repetition numbers are: {1, 2, 4, 8, 16, 32, 64, 128, 192, 256, 384, 512, 768, 1024, 1536, 2048}
“Set of PDSCH repetition numbers” and “Set of PUSCH repetition numbers” are signalled in MTC-SIB:
    Mode A: 4 values
    Mode B: 8 values
    Default values:
      Mode A: set = {1,2,4,8}
      Mode B: set = {4,8,16,32,64,128,256,512}

## Slide 5: Proposal: RRC Parameter “Number of PUCCH repetitions”
RRC parameter “Number of PUCCH repetitions” value range is according to one of the following two alternatives:
  Alternative 1: {1,2,4,6} for CE mode A, {6,12,18,24} for CE mode B.
    Supported by:
  Alternative 2: {1,2,4,8} for CE Mode A, {4,8,16,32} for CE mode B
    Supported by: Panasonic, ALU, ASB, Samsung, QC , Nokia Networks, Ericsson, Sequans, MediaTek, ZTE, Sony