## Slide 1: Way forward on TBS determination in initial partial subframes
Panasonic, ...
3GPP TSG RAN WG1 Meeting #83 Anaheim, US, 15th - 22nd November 2015
Agenda Item: 6.2.3.3
R1-157692

## Slide 2: Background
For the initial subframe, the MAC layer/scheduler needs to determine the Transport Block Size (TBS) and prepare PHY coding before knowing how long the initial subframe is
This might cause the need to prepare the MAC/PHY chain assuming two different TBS sizes or starting positions for at least the first two subframes
  Depending whether the TBS for the first subframe is size 1 or size 2, the Transport Block for the second subframe would start at different positions of the Tx buffer even for the same TBS of the second Transport Block.
In order to alleviate this burden to the eNB, it is desirable to determine only one TBS that is applicable to the first subframe, regardless of whether the first subframe is full or partial.

## Slide 3: Potential solutions
Option A)
  Re-use the DwPTS TBS determination approach with a scaling factor of 0.5, so that N_PRB = floor(N'_PRB * 0.5) for lookup in the TBS table
Option B)
  Determine the TBS according to the N'_PRB as indicated in the DCI, but adapt the modulation order in case the coderate exceeds 0.931
    E.g. if the I_MCS indicates QPSK but the coderate for the determined TBS exceeds 0.931, the modulation order is changed to 16-QAM

## Slide 4: Analysis Option A
The example assumes scheduling of 100 PRBs in a full or partial subframe
For a full subframe, the TBS table allows the following TB sizes
For a partial subframe according to Option A (PRB scaling), the following TBS sizes are allowed
Yellow elements denote TBS that are identical for full subframe and PRB scaling partial subframes.
  "36696" is also identical, but exceeds code rate 0.931 in both cases
Effect: Only 9 TB sizes are identical for a full subframe and a partial subframe with PRB scaling
The modulation size and code rate for these 9 TB sizes
2792 | 3624 | 4584 | 5736 | 7224 | 8760 | 10296 | 12216 | 14112 | 15840 | 15840 | 17568 | 19848 | 22920 | 25456 | 28336 | 30576 | 30576 | 32856 | 36696 | 39232 | 43816 | 46888 | 51024 | 55056 | 57336 | 61664 | 63776 | 75376
1384 | 1800 | 2216 | 2856 | 3624 | 4392 | 5160 | 6200 | 6968 | 7992 | 7992 | 8760 | 9912 | 11448 | 12960 | 14112 | 15264 | 15264 | 16416 | 18336 | 19848 | 21384 | 22920 | 25456 | 27376 | 28336 | 30576 | 31704 | 36696
 | TBS | 3624 | 8760 | 14112 | 19848 | 22920 | 25456 | 28336 | 30576 | 30576
Full | M | 2 | 2 | 2 | 4 | 4 | 4 | 4 | 4 | 6
 | CR | 0,151 | 0,365 | 0,588 | 0,4135 | 0,4775 | 0,53 | 0,59 | 0,637 | 0,425
Scaling | M | 2 | 4 | 4 | 6 | 6 | 6 | 6 | 6 | 6
 | CR | 0,302 | 0,365 | 0,588 | 0,551 | 0,637 | 0,707 | 0,787 | 0,849 | 0,849

## Slide 5: Analysis Option B
The example assumes scheduling of 100 PRBs in a full or partial subframe
For a full subframe, the TBS table allows the following TB sizes
For a partial subframe according to Option B (Modulation order adaptation), the same TBS sizes are allowed that show a code rate <=0.931
Effect: 19 identical TB sizes are available for a full subframe and a partial subframe with Modulation adaptation
The modulation size and code rate for these 19 TB sizes
2792 | 3624 | 4584 | 5736 | 7224 | 8760 | 10296 | 12216 | 14112 | 15840 | 15840 | 17568 | 19848 | 22920 | 25456 | 28336 | 30576 | 30576 | 32856 | 36696 | 39232 | 43816 | 46888 | 51024 | 55056 | 57336 | 61664 | 63776 | 75376
2792 | 3624 | 4584 | 5736 | 7224 | 8760 | 10296 | 12216 | 14112 | 15840 | 15840 | 17568 | 19848 | 22920 | 25456 | 28336 | 30576 | 30576 | 32856 | 36696 | 39232 | 43816 | 46888 | 51024 | 55056 | 57336 | 61664 | 63776 | 75376
 | TBS | 2792 | 3624 | 4584 | 5736 | 7224 | 8760 | 10296 | 12216 | 14112 | 15840 | 15840 | 17568 | 19848 | 22920 | 25456 | 28336 | 30576 | 30576 | 32856
Full | M | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 6 | 6
 | CR | 0,116 | 0,151 | 0,191 | 0,239 | 0,301 | 0,365 | 0,429 | 0,509 | 0,588 | 0,66 | 0,33 | 0,366 | 0,414 | 0,478 | 0,53 | 0,59 | 0,637 | 0,425 | 0,456
Mod. Adapt. | M | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 4 | 4 | 4 | 4 | 4 | 4 | 6 | 6 | 6 | 6 | 6 | 6
 | CR | 0,233 | 0,302 | 0,382 | 0,478 | 0,602 | 0,73 | 0,858 | 0,509 | 0,588 | 0,66 | 0,66 | 0,732 | 0,827 | 0,637 | 0,707 | 0,787 | 0,849 | 0,849 | 0,913

## Slide 6: Observations
With PRB Scaling, 9 identical TB sizes are available for full and partial subframes
With Modulation Adaptation, 19 identical TB sizes are available for full and partial subframes
Modulation used for TBS
  PRB Scaling
    QPSK for TBS 1384-7992
    16-QAM for TBS 7992-15264
    64-QAM for TBS 15264-31704
  Modulation Adaptation
    QPSK for TBS 2792-10296
    16-QAM for TBS 12216-19848
    64-QAM for TBS 22920 -31704
  This means that for the same TBS, Modulation Adaptation will choose the same or more robust modulation order compared to PRB scaling, resulting in a generally lower BLER for the same TB

## Slide 7: Proposal
For an initial partial subframe,
  The TBS is determined according to the I_MCS and N'_PRB as indicated in the DCI
  After determining the TBS, the effective code rate is determined for the indicated modulation order
    If that effective code rate exceeds 0.931, then the modulation order is adapted to the next higher level