## Slide 1: WF on Ych RRC Parameter for eMTC
Sony, [Ericsson, Sierra Wireless, IDC, …]
R1-157707
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda item 6.2.1.2

## Slide 2: Background on Ych
In Tuesday morning’s session, the following was agreed:
Agreement:
  X = Ych
    Note that there is no higher layer signalling for X
    The number of bits for configuring Ych is 2, and the possible values are CE mode dependent
    Note: Ych is applicable to the case when hopping is enabled and the case when hopping is disabled
    FFS the values of Ych, e.g.,:
      CE mode A:
        FDD: Ych = {1, 2, 4, 8}
        TDD: Ych = {1, 5, 10, reserved}
      CE mode B:
        Ych = {2, 4, 8 16}
        Ych = {5, 10, 20, reserved}
Task: agree on value(s) for Ych

## Slide 3: Proposal on Ych
The value of Ych is applicable to all eMTC channels to which frequency hopping is applicable
Ych is MTC-SIB signalled using 2 bits for each CE mode. The 2 bits can be used to configure the following values of Ych :
  CE mode A and paging:
    FDD: Ych = {1, 2, 4, 8}
    TDD: Ych = {1, 5, 10, 20}
  CE mode B:
    FDD: Ych = {2, 4, 8, 16}
    TDD: Ych = {1 ,5, 10, 20}
  For PRACH, RAR, Msg3, Msg4
    RACH CE levels 0,1 use Ych for CE mode A
    RACH CE levels 2,3 use Ych for CE mode B