## Slide 1: WF on Remaining PDSCH issues for eMTC
Sony
R1-157797
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th – 22nd November, 2015
Agenda item 6.2.1.4

## Slide 2: Background
Background
RAN1#82 agreement:
For HD-FDD, FD-FDD and TDD, if the UE is operating with no repetition, the same max number of DL and UL HARQ processes as for Cat-0 UE in Rel-12, except that:
  FFS if the number of DL HARQ processes should be increased for TDD with respect to that of Rel-8 for the case of no repetition
FFS the case of small coverage enhancement
Soft buffer management is based on a maximum of 8 DL HARQ processes as in Rel-8

## Slide 3: Proposal on Number of HARQ Processes for Small Coverage Enhancements for FDD
Proposal
For FDD, if the UE is operating in Mode A
  the same max number of DL and UL HARQ processes as for Cat-0 UE in Rel-12

## Slide 4: Proposal on Number of HARQ Processes for Small Coverage Enhancements for TDD
For TDD, if the UE is operating in CE Mode A:
  the same max number of UL HARQ processes as for Cat-0 UE in Rel-12
  The maximum number of DL HARQ processes is as below:
TDD UL/DL configuration | Maximum number of HARQ processes
0 | 6
1 | 9
2 | 12
3 | 11
4 | 14
5 | 16
6 | 8

## Slide 5: Proposal on PDSCH Resource Block Type (Issue 1)
VRB of distributed type is not supported

## Slide 6: Proposal on PDSCH Resource Allocation Type (Issue 2)
Mode A: only resource allocation type 0 is supported.
Mode B: Always use 6 PRB allocation.

## Slide 7: Proposal on Case 2 PDSCH Scheduling (Issue 4)
For Rel-13 low complexity UEs operating in mode A, under cross-subframe scheduling, case 2 is not supported.
For Rel-13 low complexity UEs operating in mode B, under cross-subframe scheduling, case 2 is not supported.
In case of frequency hopping, retuning occurs within 2 OFDM symbols and there is no need for a retuning subframe

## Slide 8: Proposal on PDSCH and PUSCH HARQ feedback collisions (Issue 10)
When PDSCH and PUSCH HARQ feedback occupying different narrowband collides, downselect between the options:
  Option 1: collisions avoided by eNodeB scheduling or by UE implementation (no spec impact)
  Precedence rules defined in spec: either
    Option 2A: PDSCH prioritized over HARQ ACK / NACK
    Option 2B: HARQ ACK / NACK prioritized over PDSCH

## Slide 9: Proposal on Supported Number of Antenna Ports (Issue 11)
The number of antenna ports supported in DMRS modes can be different to the number supported in CRS modes and:
For CRS modes: the number of antenna ports supported by the UE is downselected between:
  Option 1: 2 antenna ports
  Option 2: 4 antenna ports
For DMRS modes, the number of antenna ports supported by the UE is downselected between:
  Option 1: 2 antenna ports
  Option 2: 4 antenna ports

## Slide 10: Proposal on PUCCH ACK / NACK Transmission (Issue 13)
Both ACK and NACK can be transmitted on PUCCH to indicate reception status of PDSCH.