## Slide 1: WF on MPDCCH PDSCH frequency hopping relationship
Huawei, HiSilicon
3GPP TSG RAN WG1 Meeting #83 157824
Anaheim, USA, 15 - 22 November, 2015
Agenda Item: 6.2.1.2

## Slide 2: Background
Number of narrowbands for M-PDCCH/PDSCH frequency hopping | mpdcch-pdsch-HoppingNB | The number of narrowbands for M-PDCCH/PDSCH frequency hopping | 2, 4 | Cell specific
Frequency hopping activation for unicast M-PDCCH/PDSCH | mpdcch-pdsch-HoppingConfig | Frequency hopping activation/deactivation for unicast M-PDCCH/PDSCH | ON, OFF | UE specific
Frequency hopping offset for M-PDCCH/PDSCH | mpdcch-pdsch-HoppingOffset | Frequency hopping offset for M-PDCCH/PDSCH | 1, 2, …., max available narrowband | Cell specific
Agreement:

## Slide 3: Background
Agreement:
Frequency hopping configuration for M-PDCCH: the first narrowband is signaled, the other narrowband(s) are determined using a single configurable offset (cell-specific)
Agreement:
Frequency hopping configuration for PDSCH –
  The first narrowband is determined without any new higher layer configuration involved, the other narrowband(s) are determined using a single configurable offset
    The offset is cell-specifically configured, applicable to all CE levels
In CE Mode A, on/off of unicast PDSCH frequency hopping is dynamically indicated by DCI if PDSCH hopping is enabled by higher-layer signaling

## Slide 4: Proposals
For unicast DL transmission in CE mode B, the first narrowband of PDSCH is determined without any new higher layer configuration involved, by the following options
  when mpdcch-pdsch-HoppingConfig is OFF,
    the same as M-PDCCH narrowband
  when mpdcch-pdsch-HoppingConfig is ON,
    the same as the narrowband that the nearest associated M-PDCCH can hop to, i.e. with an offset from the nearest associated M-PDCCH narrowband given by
    mpdcch-pdsch-HoppingOffset