## Slide 1: WF on SI Scheduling
Nokia Networks, ALU, ASB, Ericsson, Intel, LGE
R1-157828
3GPP TSG RAN WG1 #83
Anaheim, USA, 15th – 22nd November, 2015
Agenda item 6.2.1.9

## Slide 2: Background
Agreements from RAN1#81 –
  The number of resource blocks used for MTC SIB transmission is fixed to 6 PRBs.
  Scheduling information for MTC SIBs other than SIB1bis are given in SIB1bis.
  The number of repetitions for MTC SIBs other than SIB1bis is configurable by the network.
    FFS: How the network will signal the number of repetitions
Agreements from RAN1#82bis –
  The maximum number of SI messages that can be acquired across SI windows is 4
Agreements from RAN2#91bis –
  A new value range of si-WindowLength is defined for Rel-13 LC/CE UEs. Value range is {20, 40, 60, 80, 120, 160, 200} ms. FFS whether larger values might be needed for TDD.

## Slide 3: Proposal
Scheduling information for an SI is given by –
  Narrowband index
    All the 6 PRBs in the narrowband are used
  MCS
    QPSK is always used
    TBS
      FFS values {152, 208, 256, 328, 408, 504, 600, 712, 808, 936}
  Subframe offset to indicate the starting subframe (relative to the start of the SI window)
    FFS values {0, 1, 2, 3, 4, 5, 6, 7, 8, 9}
  Number of repetitions within SI window
    FFS values {1, 2, 4, 8, 16, 32, 64, 128}
  Time interval between repetitions
    FFS values {1, 10, 20, 40} ms

## Slide 4: Examples
Example 1
Example 2

## Slide 5: Proposal
In case of collision between SI transmissions and M-PDCCH/PDSCH repetitions,
  Drop M-PDCCH/PDSCH subframe, the unavailable subframe is counted in the repetition