## Slide 1: Way Forward on Scrambling Initialization
Spreadtrum, NEC
R1-157849
3GPP TSG RAN WG1 Meeting #83
Anaheim, Usa, 15th – 22nd November 2015
Agenda item 6.2.1.5

## Slide 2: Background
R1-157333, Discussion on open issues in MTC PDSCH, Spreadtrum Communications
R1-156683, Extending the Scrambling sequence for DL/UL transmissions, NEC

## Slide 3: Background
Agreement:
For PUSCH and PDCSH RV cycling,
  Rel 13 UE in Mode A: Z=1
  Rel 13 UE in Mode B:
    For FDD: Z=4
    For TDD PUSCH Z = 5, PDSCH Z= 10
In Mode A and Mode B, PUSCH/PDSCH scrambling sequence is different in every Z subframes for the duration of repetitions
Note: the set of Z subframes correspond to all subframes in any frame, regardless of whether the subframes are valid or not for PUSCH/PDSCH transmission

## Slide 4: Proposal 1
  For PDSCH/PUSCH scrambling initialization value is calculated:
    Option A:
    nfr = SFN % nfr,max
    nfr,max is number of frames required for max R
    Max R 1024 -> nfr,max = 128
    Codeword index q is reused for one bit of nfr
    For mode B the calculation above is applied only for first subframe of period Z
    Option B:
      Where
      Use MSB bit to differentiate legacy and eMTC UEs
      For mode B, is the first slot of the first subframe of period Z

## Slide 5: Proposal 2
  Alt1:
  In Mode A and Mode B, DMRS scrambling sequence is different in every Z subframes for the duration of repetitions
  For DMRS scrambling initialization value is calculated:
    nfr = SFN % nfr,max
    nfr,max is number of frames required for max R
    Max R 1024 -> nfr,max = 128

## Slide 6: Proposal 2
  Alt2:
  In Mode B, DMRS scrambling sequence is same in Z subframes
  The DMRS scrambling initialization value is calculated as:
      is the first slot of the first subframe of period Z
      Changes are only for Z subframes and no change for long repetitions