## Slide 1: WF on remaining issues of random access procedure
Ericsson, Lenovo
3GPP TSG RAN WG1 Meeting #83 R1-157858
Anaheim, USA, 15 - 22 November, 2015
Agenda Item: 6.2.1.10

## Slide 2: Proposals for Msg3/Msg4
Background [RAN1 #83 agreements]
The narrowband index of M-PDCCH for Msg3 re-transmission or Msg4 transmission is determined by down-selecting one of the following (no additional higher-layer impact)
  Alt 1: implicitly derived by the preamble index of the last successful PRACH attempt
  Alt 2: indicated in RAR using 2-bit, as part of the RAR UL grant
  Proposal assuming 2 bits in RAR are available for M-PDCCH narrowband indication for Msg3 retransmission and Msg4:
    NB_RAR = narrowband used for first subframe of M-PDCCH for RAR
    NB_Msg34 = narrowband used for first subframe of M-PDCCH for Msg3 retransmission and first subframe of M-PDCCH for Msg4
    N_NB = the total number of DL narrowbands in the system bandwidth
    Bits=00  NB_Msg34 = (NB_RAR + 0) mod N_NB
    Bits=01  NB_Msg34 = (NB_RAR + 1) mod N_NB
    Bits=10  NB_Msg34 = (NB_RAR + 2) mod N_NB
    Bits=11  NB_Msg34 = (NB_RAR + 3) mod N_NB
  Alternative proposal if up to 4 bits would be available for M-PDCCH narrowband indication for Msg3 retransmission and Msg4:
    The up to 4 bits indicate the narrowband