## Slide 1: WF on Remaining Issues on Number of Repetitions
Sony, Ericsson
R1-157865
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda item 6.2.1.6

## Slide 2: Background on 4-bit indicator
RRC parameter name for 4-bit indicator has been agreed in RRC parameter list:
Downlink:
Maximum value to indicate the set of PDSCH repetition number for CE mode A
Maximum value to indicate the set of PDSCH repetition number for CE mode B
Uplink:
Maximum value to indicate the set of PDSCH repetition number for CE mode A
Maximum value to indicate the set of PDSCH repetition number for CE mode B

## Slide 3: Proposal on repetitions for Mode A
  For Mode A, the 4-bit indicator provides an index to a table
Maximum value to indicate the set of PxSCH repetition number | Set of repetitions
no IE in MTC-SIB (default) | 1,2,4,8
16 | 1,4,8,16
32 | 1,4,16,32

## Slide 4: Proposal on repetitions for Mode B
  For Mode B, the 4-bit indicator provides an index to a table
Maximum value to indicate the set of PxSCH repetition number | Set of repetitions
No IE in MTC-SIB (default) | 4,8,16,32,64,128,256,512
192 | 1,4,8,16,32,64,128,192
256 | 4,8,16,32,64,128,192,256
384 | 4,16,32,64,128,192,256,384
512 | 4,16,64,128,192,256,384,512
768 | 8,32,128,192,256,384,512,768
1024 | 4,8,16,64,128,256,512,1024
1536 | 4,16,64,256,512,768,1024,1536
2048 | 4,16,64,128,256,512,1024,2048