## Slide 1: WF on PUCCH Handling With Retuning
LG Electronics, ...
R1-157869
3GPP TSG RAN WG1 #83
Anaheim, USA, 15th – 22nd November, 2015
Agenda item 6.2.1.6

## Slide 2: Background
Working assumption (to be automatically confirmed by Saturday if no issues are found):
Cases for UL retuning to consider:
  Case 1: UE retunes from PUSCH narrowband to PUSCH narrowband
  Case 2: UE retunes from PUCCH narrowband to PUCCH narrowband
  Case 3: UE retunes from PUCCH narrowband to PUSCH narrowband
  Case 4: UE retunes from PUSCH narrowband to PUCCH narrowband
  Case 5: UE retunes from PRACH narrowband to PRACH narrowband
Options for how to define the UL retuning gap:
  Option A: Last two symbols of the earlier subframe
  Option B: Last symbol of the earlier subframe + first symbol of the later subframe
  Option C: Guard subframe (not needed according to results in R1-157472)
  Option D: First two symbols of the later subframe
Agree on the following:
  Case 1: Option B
  Case 2: Option B
  Case 3: Option D
  Case 4: Option A
  Case 5: FFS

## Slide 3: Background
Issues in case of multiplexing UEs’ PUCCH with different transmission pairs

## Slide 4: Proposal to handle PUCCH retuning
A UE always uses shortened PUCCH format in every potential hopping instance regardless of actual necessity of retuning.
  E.g., in subframe n in SFN i where (( i * 10 + (n-1)) % Ych = 0), shortened PUCCH format (puncture last OFDM symbol) is used, in subframe n+1, shortened PUCCH format (puncture the first OFDM symbol) is used)
  The symbol saved by shortened PUCCH can be used for retuning gap if necessary
If the above retuning gap is not sufficient, take the retuning gap by puncturing PUSCH or SRS
  SRS is lowest priority
  When two PUSCH is used, puncture one symbol from each PUSCH