## Slide 1: WF on remaining issues of random access procedure
Huawei, HiSilicon, Lenovo
3GPP TSG RAN WG1 Meeting #83 R1-157884
Anaheim, USA, 15 - 22 November, 2015
Agenda Item: 6.2.1.10

## Slide 2: Proposal
DCI contents | Field size for CE mode A | Field size for CE mode B | Description
Msg3 narrowband index | ceil(log2(number of narrowbands)) | 2 | NB index of Msg3 scheduling
PRB assignment | 4 | 3 | PRB location within the configured narrowband in narrowband index field.
Repetition number | 2 | 3 | The repetition level of Msg 3 is dynamically indicated based on a set of values configured by higher layers.
MCS | 3 | 2 | MCS/TBS
TPC | 3 | 0 | TPC is supported in CE mode A
A-CSI | 1 | 0 | A-CSI is supported in CE mode A
UL delay | 1 | 0 | 
Msg3/4 M-PDCCH narrow band index | 2 | 2 | NB index of M-PDCCH scheduling Msg3 ReTx and Msg4
Total | 20 | 12 | 

## Slide 3: Proposal
  X=max{ceil(log2(number of narrowbands)), 2}, wherein the X bits indicating the M-PDCCH narrowband scheduling Msg3 ReTx and Msg4
  The first two left bits in X bits are the 2 bits indicated by the field “Msg3/4 M-PDCCH narrow band index” in UL grant of RAR
  The remaining (X– 2) bits are implicitly derived from PRACH preamble index
X | The leftmost two bits indicated in UL grant | The rightmost (X-2) bits derived from Preamble index
2 | 2 | 0
3 | 2 | 1
4 | 2 | 2
The rightmost (X-2) bits derived from Preamble index | The relationship between PRACH index and right most (X-2) bits
0 | N/A
1 | 0: Preamble index mod 2=0 1: Preamble index mod 2=1
2 | 00: Preamble index mod 4=0 01: Preamble index mod 4=1 10: Preamble index mod 4=2 11: Preamble index mod 4=3