## Slide 1: WF on Remaining Details on paging for DCI
Qualcomm, Panasonic

## Slide 2: Proposal (Paging)
DCI contents | Scheduling Paging
S_flag | 1
Narrowband index | Ceil(log2(number of narrowbands))
MCS | 3 (truncated MCS)
Repetition number (PDSCH) | 3/2 (from predefined set of repetition numbers)
M-PDCCH repetition number | 2

## Slide 3: Interpretation of PDSCH repetition level
From a set of 16 repetition numbers for PDSCH R1,…, R16, the 3-bit repetition number for PDSCH selects between the following
  If MPDCCH repetition 00: {R1,…,R8}
  If MPDCCH repetition 01: {R3,…,R10}
  If MPDCCH repetition 10: {R6,…,R13}
  If MPDCCH repetition 11: {R9,…,R16}
Alternative: 2-bit repetition number
  If MPDCCH repetition 00: {R1,…,R4}
  If MPDCCH repetition 01: {R4,…,R7}
  If MPDCCH repetition 10: {R8,…,R12}
  If MPDCCH repetition 11: {R12,…,R16}