## Slide 1: mmWave Channel Measurement Results on UMi Street-canyon and Open-square
Samsung
3GPP TSG-RAN WG1 #84
St. Julian’s, Malta, February 15 – 19, 2016
Agenda item: 7.3.5.4
Document for : Information
R1-160592

## Slide 2: Background
In RAN#69, the SID for above 6GHz channel modelling was approved, and the following email-discussion was conducted.
  In UMi scenario, street-canyon and open-square are considered for above 6 GHz spectrum bands.
Samsung conducted the field measurement campaigns & ray-tracing simulation in UMi scenarios at 28 GHz to analyze the mmWave channel characteristics.
  Derive the preliminary SCM channel parameters

## Slide 3: 28 GHz Measurement Campaign – Urban Area / Street Canyon [1]
Synthesized Omni-directional Measurements in Urban Street-canyon Environment (Daejeon, Korea)
  38 valid NLoS measurements at different positions , repeated 50 measurements
  Tx : 15m height
  Rx : 1.6m height (at NLoS conditions)
Channel Sounder
  Carrier frequency : 28 GHz
  Transmit power : 29 dBm
  TX /RX antenna gain : 24.5 dBi ( 10 degree 3dB beamwidth )
  PN-sequence rate : 250 M chip/sec
  Polarization : vertical linear polarization
  Maximum measurable pathloss : 160 dB
        ( Dynamic range : 60 dB )

## Slide 4: 28 GHz Measurement Campaign (w/KT) – Resort Town [2]
Tx #1
05
06
08
10
11
15
17
19
20
21
22
Tx #2
27
28
29
146dB
139dB
134dB
137dB
140dB
121dB
113dB
131dB
130dB
137dB
123dB
132dB
137dB
143dB
100m
200m
Tx #1:Balcony at 7th floor
Ski Resort town
  close to UMi street-canyon
14 NLoS valid samples
(blocked by object, building, tree in NLoS)
  Distance range : 51 m ~ 207m
Pathloss analysis
  Marked On the map (over 200 m)
Delay / Angular spread analysis conducted
uN005
Tx #2:Balcony at 3rd floor

## Slide 5: 28 GHz Measurement Campaign (w/KT) – Open-area in Resort Town
Analysis on Power Angular-Delay Spectrum
  Plot the received power / directional PDP over each azimuth angle arrival
[Example] Rx NLoS #8 Measurement
  Tx-Rx link-distance = 207 m
  Decent signal power reception over 200m range
  Dominant paths are reflected from around buildings
  Exists few paths due to the environment of street-canyon environment
NLoS #8
Tx #1
Tx placed behind the building/tree

## Slide 6: 28 GHz Channel Characteristics
Pathloss model with fixed SF factor

## Slide 7: 28 GHz Channel Characteristics
Large-scale Parameter Analysis (Daejeon Urban, PyeongChang Resort Town)
Delay Spread in NLoS
  95% of DS = 150~200 ns
  50% of DS = 40~50 ns
  Median of DS in 28 GHz is smaller than the statistics below 6 GHz (Median of DS in TR36.873 = 129 ns)
Rx Azimuth Angle Spread in NLoS
  Following log-normal distribution
  Median of ASA (Angle Spread of Azimuth Arrival) = 30 ~ 40 deg
  (Median of ASA in TR36.873 = 69 deg)

## Slide 8: 28 GHz Channel Characteristics
All parameters used are similarly defined in 3GPP 3D-SCM and derived based on clusters .
  For example, the KPowerMeans (KPM) algorithm is used for automatic clustering of the measured MPCs at a given location. (We chose delay scaling factor =5)
Cumulative distribution functions (CDFs) of the number N of clusters
  The positive Poisson distributions are overlaid as the best fit for urban measurement data.

## Slide 9: Manhattan 28 GHz Measurement Campaign
Extensive Measurement Campaign @ NYU campus, Manhattan
  Prof. Rappaport team conducted 28GHz band field measurements
  33 measurement samples (in various env.)
  Proposed spatial mmWave channel model based-on measurement data

## Slide 10: Measurement & Ray-tracing @ Manhattan
3D ray-tracing simulation @ NYU Campus, Manhattan [3]
  Build up the geometry model in the same area (including vegetation)
  The ray-tracing data is obtained after verifying & comparing with the measurement
TX
TX

## Slide 11: Verification on Ray-tracing (w/ NYU Measurement)
Same locations selected in ray-tracing
Location #2 : Tx COL1 – Rx5
  NLoS (heavily obstructed) condition
  Power-angular plots
Angle Spread (RX)
NYU Measurement | Ray-tracing Result
39.12 ° | 45.06 °
TX pointing angle: 264°
TX beamwidth: 10°
RX: Omni-directional
[sources from NYU Wireless ]
NYU Measurement – Rx azimuth AoA
Ray-Tracing – Rx azimuth AoA

## Slide 12: Channel Model Parameters : Large-scale Parameters - based on Ray-tracing Simulation [3]
 |  | UMI Street-canyon (28 GHz) |  |  |  | UMa Street-canyon (28 GHz) | 
 |  | Daejeon |  | NYU Campus |  | NYU Campus | 
 |  | LoS | NLoS | LoS | NLoS | LoS | NLoS
log(DS) | μDS | -7.67 | -7.31 | -7.05 | -6.91 | -6.97 | -6.80
 | σDS | 0.30 | 0.60 | 0.44 | 0.54 | 0.50 | 0.72
log(ASD) | μASD | 1.15 | 0.82 | 1.18 | 0.94 | 1.07 | 1.21
 | σASD | 0.46 | 0.42 | 0.47 | 0.66 | 0.54 | 0.68
log(ASA) | μASA | 1.23 | 1.35 | 1.51 | 1.48 | 1.49 | 1.51
 | σASA | 0.34 | 0.42 | 0.27 | 0.43 | 0.38 | 0.42
Delay distribution |  | Exponential |  |  |  |  | 
AoD/AoA distribution |  | Wrapped Gaussian |  |  |  |  | 
ZoD/ZoA distribution |  | Laplacian |  |  |  |  | 
Delay scaling |  | 2.82 | 2.06 | 2.62 | 2.10 | 2.78 | 1.98
Number of Cluster | N | 6 | 6 | 6 | 6 | 6 | 6
Number of Subpath | M | 10 | 10 | 10 | 10 | 10 | 10
Cluster ASD |  | 2.7 | 5.7 | 2.5 | 2.9 | 1.9 | 4.8
Cluster ASA |  | 3.3 | 6.7 | 2.9 | 3.5 | 2.7 | 6.8

## Slide 13: Comparison of Proposed mmWave Channel Model
Channel Output in DS / AS (in Daejeon)
  Compared with
    Measurement Data
    Ray-tracing observations
    Channel Model Output

## Slide 14: Conclusions
From the measurement conducted in UMi street-canyon at 28 GHz, the pathloss model (up to 200 m range) is developed
  Similar pathloss slope around 3.6 (i.e, pathloss exponent) compared to the pathloss model in TR36.873
Delay / angular spread in 28 GHz UMi are also analyzed with the measurement campaigns
  Smaller DS and AS than the LSPs in TR36.873
Ray-tracing results are used for deriving most of channel parameters
  Daejeon Urban / NYU Campus ray-tracing results were verified with the measurement data
  Ray-tracing-based channel model parameters at 28 GHz are available as an extension of 3D-SCM modeling framework, which is reasonably well matched

## Slide 15: References
[1] S. Hur, Y.-J. Cho, T. Kim, J. Park, A. F. Molisch, K. Haneda, M. Peter, “Wideband Spatial Channel Model in an Urban Cellular Environments At 28 GHz,” in Proc. European Conference on Antennas and Propagation (EuCAP), April 2015.
[2] J. Ko, S. Hur, S. Lee, Y. Kim, Y. Noh, Y. Cho, S. Kim, S. Bong, S. Kim, J. Park, D. Park, D. Cho, “28 GHz Channel Measurements and Modeling in a Ski Resort Town in Pyeongchang for 5G Cellular Network Systems,” will be presented in European Conference on Antennas and Propagation (EuCAP), April 2016
[3] S. Hur, S. Baek, B. Kim, Y. Chang, A. F. Molisch, K. Haneda, T. Rappaport, J. Park, “Proposal on Millimeter-Wave Channel Modeling for 5G Cellular System,” will be published IEEE Journal of Selected Topics in Signal Processing, April 2016.